New Features of BDS C v1.5:
                    A Summary for Users of Pre-1.50 Versions

                                   Leor Zolman
                                   BD Software
                                   P.O. Box 9
                         Brighton, Massachusetts, 02135
                                 (617) 782-0836
                                        


         WARNING! Version 1.5 of the  BDS  C Compiler will not work under
       pre-2.x versions of the CP/M  operating  system.  In order to take
       full  advantage  of  CP/M 2.x I/O mechanisms  without  introducing
       really  painful  configuration  complications, compatibility  with
       CP/M  1.4 (or earlier versions) has been  sacrificed.   Users  who
       cannot upgrade their  CP/M's to version 2.x must go on using v1.46
       of the compiler.  Sorry about that.) 




             You Can Now Get BDS C From Vendors Other Than Lifeboat


    So  far,  the  only  definite alternative distributor is the BDS C  User's
  Group.  I  am  at  a  very  flexible position  right  now  regarding  dealer
  distribution    arrangements,   and   welcome   inquiries   from   potential
  distributors.  I'm not going to go running  to  every outfit that advertises
  in BYTE and beg them to sell the compiler, simply because  I'm  not sure how
  much  of  a hassle I'd be signing up for by that behavior.  Rather, I'd like
  to see small-scale hacker types involved in  distribution, so that end-users
  can  have a prayer of receiving INTELLIGENT customer service.  Gads, anytime
  I get  to  rambling  about  something interesting I begin to wonder if it is
  bordering on a commercialistic exploitation of the ARPA net!????  To play it
  safe: if anyone reading this paragraph objects  to the content, feel free to
  delete it from this file. 












                                      - 1 -                                   













                            New Command Line Options


    CLINK now takes a new  option,  -n, which causes the resulting COM file to
  not  perform  a  warm-boot  after  it  is finished executing.   This  option
  performs the function that v1.46's  NOBOOT.C  program  had been doing.  Note
  that when -n is used,  there  is approximately 2K less user memory available
  because the CCP is not overwritten. 

    CC (formerly named  CC1) now takes the option -k, to activate the Kirkland
  debugger  mechanism.  This  causes  a  special  symbol  table  file  (having
  extension .CDB) to be written  to  disk, and causes the compiler to generate
  special restart instructions at the  start  of  every  statement to interact
  with David Kirkland's C debugger package.  The  debugger may not be included
  on the distribution disk for  space limitation reasons, but is available for
  nominal cost-of-media cost from the  BDS  C User's Group or from BD Software
  (on 8" disk) via special arrangement. 




                      Functional Changes to Major Commands


    CLINK now automatically loads all functions, by  default,  from  each  CRL
  given on the command line in a  linkage.   The  -f option is now reversed in
  sense from previous versions, and operates  exactly  the  same  as  L2's  -l
  option...i.e.,  -f  appearing on a CLINK command line causes all  CRL  files
  named after it  to  be  scanned instead of loaded, while all CRL files named
  before the  -f  flag  are  loaded.  This makes the general format of a CLINK
  command line be:

          A>clink <main file> [<other files in prog>] [-f <lib files>] <cr>

  Other options may be interspersed in the command line, of course. 




                         New Low-Level File I/O Features


    -   All the low-level file I/O now uses the CP/M 2.2x  random-record  read
       and  write  calls.  Therefore, files may be up to 8 megabytes in length
       instead of only up to 256K bytes. 

    -  The "seek" function may be given an origin  code  of 2, meaning to seek
       relative to the end of the file.  Note that the offset must be negative
       in this case to make sense, since it is always added to the base, which



                                      - 2 -                                   









       in this case is the end of the file.  For example, the  following  call
       seeks to the next-to-last sector in the file:

               seek(fd, -2, 2);        /* seek to 2nd sector from end of file */

    -  User number prefixes are now accepted wherever a filename  argument  is
       called for.  Such  a  prefix consists of a decimal number between 0 and
       31, followed immediately by a slash (/) character and then the filename
       (with or without an optional  disk  designator).   This causes the file
       I/O mechanism to switch into the user area associated  with  each  file
       for the duration  of any I/O operation involving that file, then switch
       back  to  the current user area when done.  Any filename may  now  take
       either an explicit disk designator, an explicit user area, or both.  If
       both are given, then the  user area specification must precede the disk
       designator.  Here is an example:

               if (open("0/A:DATABASE.DAT",2) == ERROR)
                       exit(puts("Can't open the database, turkey. \n"));

       Note  that  this allows programs in separate user areas to manipulate a
       common  data  file  kept  on  one  particular   drive  and  user  area,
       eliminating the need to have a separate copy of the data file  in  each
       user area  needing it.  If you are running the "ZCPR" public-domain CCP
       replacement program for CP/M, or any shell  (such as "MicroShell") that
       searches  special  drives  and  user areas for command files, then that
       feature  combined  with the user-area  enhancements  to  the  file  I/O
       library allow a very efficient utilization of the CP/M filesystem. 

    -  There are some new  functions  that  provide better diagnosis of errors
       caused by low-level file I/O calls.  Whenever a call such as open, read
       or  write  returns  a  value  of  -1 (ERROR), the errno function may be
       called to return  a  more  detailed  error  description code explaining
       exactly  what  went wrong.  The errmsg function may be used to return a
       pointer to a string corresponding to the error value returned by errno.
       A typical usage of these functions is as follows:

               i = read(fd, buffer, 20);       /* try to read 20 sectors */
               if (i == ERROR) {               /* if an error occurred...*/
                       printf("\n%s -- ABORTING THIS PROGRAM.",
                                       errmsg(errno));
                       exit();
               }




                     New Library File Searching Capabilities


    Both the compiler and linker (CC and CLINK) now have the ability to search
  for  library files in a default CP/M  drive  and  user  area,  sometimes  in
  addition  to  the  currently-logged  drive  and  user  area.   If  the  user
  configures CC and  CLINK  as  described  in the configuration section below,



                                      - 3 -                                   









  then CC will know to search a default directory for included  files named in
  angle  brackets,  and  CLINK  will  know to search a default  directory  for
  library  files.   Also, if a CRL file is named on the CLINK command line and
  CLINK cannot find that file in  the  current  drive  and user area, then the
  default area (as configured) will be searched for that file. 

    CLINK now accepts user area prefixes on CRL filenames given on the command
  line  (except  for  the  main  CRL file, which must be in the  current  user
  area.)  If an explicit disk drive and/or user area specification is given on
  the  CRL  filename  to  CLINK,  then the default area will not  be  searched
  automatically.  This is so that if an  explicit user area is given for a new
  test  version  of a CRL file, and a similarly named CRL file exists  in  the
  default library area, then the one in the default area will not be  used  if
  the explicitly named one is not found. 




                                  Configuration


    BDS  C  commands should simply come up  running  under  any  CP/M  system,
  without  any  special  configuration procedure necessary.  There are several
  optional  features  of the compiler and linker that may be configured by the
  user to increase the flexibility  of  the package.  This subsection explains
  each of those options and how to select them. 




  If Running MPM II:


    If you are running BDS C under  MP/M II, you must re-assemble the run-time
  package  with  the  "MPM2" symbol equated to 1 (it comes configured  to  0).
  Simply edit the CCC.ASM file,  assemble  it  using  ASM,  use LOAD to create
  CCC.COM, then rename that to C.CCC.




  CC and CLINK configuration


    There  are  several  user-configurable  features in CC.COM  and  CLINK.COM
  controlled by a specific bytes of memory very close to the beginning of each
  command  file.  In order to change these features, use DDT or  SID  to  read
  CC.COM  or CLINK.COM into memory (noting the length of the file printed upon








                                      - 4 -                                   










  successful loading 1),  make the changes using the s command, hit control-C,
  and  use the CP/M SAVE command to write the modified command back to  disk. 
  Make sure to have your master distribution disk safely tucked away somewhere
  before attempting these modifications! 

    Both  CC.COM  and  CLINK.COM  contain  an identically structured four-byte
  configuration block.  The base address of the block for CC.COM is 0155h, and
  for CLINK it is 0103h. The contents of the block are as follows:

          Addr.   Function                                Default value

          base+0  Default library disk                      FF  (current)

          base+1  Default library user area                 FF  (current)

          base+2  Disk where SUBMIT files are processed     00  (disk A)

          base+3  Poll console for interrupts (0 or 1)      01  (enabled)

    Note that each item in the block is exactly one byte in length.  The first
  two items specify a default disk and user area  to  be treated as a "library
  directory" by CC and CLINK. For CC, the library directory specifies where to
  find the files named in #include directives when the filename is enclosed in

  angle  brackets  2,  and also where to find CC2.COM for the second phase  of
  compilation.   For  CLINK,  this  says  where  to  find  the files DEFF.CRL,
  DEFF2.CRL, DEFF3.CRL (if present) and C.CCC.

    For the  default library disk, a value of 0 specifies drive A, 1 specifies
  drive  B,  etc.,  and  a  value  of  FFh  (255 decimal) specifies  that  the
  currently-logged  disk is to be used as the default library disk.   For  the
  default  library  user  area,  the values 0-15 denote the corresponding user
  area, and  a value of FFh (255 decimal) specifies that the current user area
  is to be the default library user area.  Both the library disk and user area
  come configured to FFh; thus, the distribution version of the v1.50 compiler
  and linker behave the same as earlier versions, in  which  the current drive
  and user area were always assumed to contain the library files by default. 



  ----------

  1. To convert the hex address printed  by DDT or SID for the last address of
  the  file into the decimal number you must give to the SAVE command, use the
  following algorithm: take the leftmost  two  hex  digits,  and compute their
  decimal equivalent (e.g.,  3C80  yields  3C,  which  is  60 decimal).  Then,
  subtract 1 from that if the rightmost two digits are 00. The final result is
  the number to give SAVE.

  2.  Filenames  enclosed in double quotes always cause the #include directive
  to   search  the  current  directory  for  the  named  file,  regardless  of
  configuration



                                      - 5 -                                   









    The third location designates which CP/M drive contains the  $$$.SUB  file
  that exists during  "Submit  File"  processing.  CLINK always tries to erase
  pending submit files when an error occurs, while CC only tries to do so when
  the -x option is given.  Since most systems always place the $$$.SUB file on
  drive  A,  that is the way CC and CLINK come configured by default.  But, if
  the user  has  customized  his system to put the $$$.SUB file on the current
  drive  instead of always on A:, then the byte pointed to by the  address  in
  these locations should be changed from 01 to 00.

    The  fourth and final location in the configuration block is a simple flag
  telling CC or CLINK whether or not  the  system console should be polled for
  the  interrupt  character  (^C) during execution of the command.  If enabled
  (non-zero), then any input typed on the console by the user during execution
  of the command will be ignored unless ^C is typed, in which case the command
  will be immediately aborted  and  control  will return to command level.  If
  disabled  (zero), then the console will never be polled.  This is useful for
  certain interrupt driven systems that  need  to recognize type-ahead and can
  handle  interruption  on  their  own  without  needing  to be polled by  the
  currently executing transient command. 

    This configuration scheme allows  users  with large-capacity disks to pick
  some particular drive and user area in which to keep all standard header and
  library  files.  The library disk and user area bytes should  be  considered
  together as a unit; if you change one,  you'll  probably  want to change the
  other also. 

    Note that CC2.COM does not need to be configured; CC.COM passes it all the
  relevant information upon transfer of control. 




























                                      - 6 -