4.4. 8086/8088

If  you  need to install Kermit on your PC, and you do not have a Kermit floppy
but you do have access to a mainframe computer with a copy of the IBM PC Kermit
distribution, you should read this section.

Kermit for the IBM PC is written in  assembly  language.    The  PC  assembler,
however, is not provided with the minimum system, so IBM PC users cannot be ex-
pected to have it.  Assembler source plus the runnable version (.EXE) of Kermit
               19
are distributed  , along with some special "bootstrap" files, described below:

The KERMIT.EXE file is converted by an assembler program on the PC, KFIX, which
makes  all  bytes  in the file printable by breaking each one up into two 4-bit
"nibbles" and adding a constant.    The  result  is  a  printable  file  called
KERMIT.FIX.    It is assumed that a copy of KERMIT.FIX is available to you on a
mainframe computer.  To download the file to the PC, two  cooperating  programs
are  run: a Fortran program, KSEND, on the mainframe and a Basic program, KGET,
on the PC.  These programs are very short; they are  shown  in  their  entirety

_______________

  19
    The  PC  assembler's  object  (.OBJ) files are not printable, like CP/M hex
files, so the Kermit-80 bootstrapping technique would not work here.

                                    - 42 -


below.  KSEND reads a line at a time from KERMIT.FIX, types the line, and waits
for  a  signal  from KGET that it can send more data.  KGET reads each line and
converts the text back to the format of an executable (.EXE) file.  Here's  the
procedure:

   1. You  should  have  a  version  of  KGET  on  the PC and KSEND on the
      mainframe; if you don't have them, copy  them  (i.e. type  them  in,
                     20
      using an editor  ) from the listings below.

   2. Log  in  on the mainframe.  This could be tricky if you have no ter-
      minal  emulation  facility  on  the  PC.    If  you  have  the   IBM
      asynchronous  communication  package,  you can do this at low speeds
      (baud rates).  If your PC has no terminal emulation facility, you'll
      have to use a real terminal to log in, and then switch the cable  to
      the PC.

   3. Compile  KSEND.FOR on your mainframe, if it needs compiling.  Define
      logical unit numbers 5 and 6 to be  the  controlling  terminal,  and
      logical unit number 7 to be KERMIT.FIX.  On the DEC-20, for example:

          @define 5: tty:
          @define 6: tty:
          @define 7: kermit.fix

      On a DECsystem-10, do something like:

          .assign tty: 5:
          .assign tty: 6:
          .assign dsk: 7:
          .rename for007.dat=kermit.fix

      On an IBM system under VM/CMS,

          .filedef 5 term ( lrecl 64 recfm f
          .filedef 6 term ( lrecl 64 recfm f
          .filedef 7 disk kermit fix ( lrecl 64 recfm f perm

      Start KSEND on the mainframe.  It will print a message, and then sit
      and  wait for the PC to send back an OK; don't change any connectors
      until you see the message.

   4. Escape back to the PC, or connect the PC to the mainframe.  The PC's
      communication port should be connected with a null  modem  cable  to
      the  modem  that's  connected  to  the mainframe (dialup, dedicated,
      switched, whatever hookup you normally have available for logging in
      on the mainframe from a terminal).  If you were  using  a  different
      terminal  to  log in to the mainframe, make sure the PC's communica-
      tion port is set at the same speed.

   5. Enter BASIC and run KGET on the PC.  If KGET prints  messages  about

_______________

  20
    You'll also have to compile and load the Fortran program on the mainframe.

                                    - 43 -


      i/o  errors,  run  it again.  If it still gets errors, reboot the PC
      and try again.  Once KGET is running, the transmission  will  begin.
      KGET will print each 64-character line of nibbles as it arrives from
      the  mainframe.  Each line should be the same length -- if you see a
      ragged edge, you can assume there has been a transmission error, and
      you should start the process again.

   6. When transmission is complete, you'll see the BASIC  "Ready"  prompt
      again.    Leave  BASIC  by  typing  SYSTEM.    You  should  now have
      KERMIT.EXE on your PC.  Try to run it.  If you see the  "Kermit-86>"
      prompt,  try  to  CONNECT  to  the  host mainframe and transfer some
      files.  If Kermit doesn't run correctly, there may have been  trans-
      mission  errors,  in  which  case you should start the process again
      from step 2 above.

This is the mainframe side, KSEND, in transportable Fortran (it should  run  on
both DEC and IBM mainframes):

C KSEND -- Download a file over the terminal line. No special checking is done,
C except to wait for response (any response at all) from other side.
C
C This Fortran program should be run on the mainframe in conjunction
C with the KGET program on the IBM PC to transfer KERMIT.FIX to the PC.
C
C Daphne Tzoar, CUCCA, Jan 83

      INTEGER A(64)

      WRITE(6,50)
50    FORMAT(' Ready to transfer data......')

C - Get terminal handshake
100   READ (5,10,END=35)X
10    FORMAT(A1)

C - Get line from file
35    READ (7,20,END=90)A
20    FORMAT(64A1)

C - Write to tty
      WRITE (6,25)A
25    FORMAT(' ',64A1,';')
      GOTO 100
90    CONTINUE

C - Send final handshake
      WRITE (6,30)
30    FORMAT(' ',65('@'))
      STOP
      END

The  final @'s tell KGET that the transmission is done.  This works because the
technique for forming KERMIT.FIX ensures that the file will contain no @'s.

This is the PC side, KGET, in PC Basic.  Note that the  communication  port  is
opened at 4800 baud (you could substitute any other speed).

                                    - 44 -


1   'KGET.BAS

5   'Run this program on the PC in conjunction with a Fortran program on the
6   'mainframe to get Kermit to the PC.  Daphne Tzoar, CUCCA, Jan 83

10   OPEN "com1:4800,n,8,1" AS #1  ' Clear the port status.
20   CLOSE #1
30   OPEN "com1:4800,n,8,1,cs,ds,cd" AS #1 ' Open it for real.
40   OPEN "KERMIT.EXE" FOR OUTPUT AS #2
50   OK$ = "ok"
60   PRINT#1,OK$                   ' Tell host we're ready for data
70   X$=INPUT$(65,#1)              ' Data plus semi-colon
80   VALUE$ = LEFT$(X$,1)          ' First char of input
90   VALUE = ASC(VALUE$)
100  IF VALUE = 64 OR VALUE = 192 GOTO 430          ' @ means we're done
110  IF VALUE >= 160 AND VALUE <= 175 THEN GOTO 140 ' Kill all illegal chars
120  IF VALUE >= 32 AND VALUE <= 47 THEN GOTO 140
130  X$ = MID$(X$,2) : GOTO 80
140  IF VALUE <> 174 GOTO 210      ' Not a dot (for read) - don't worry
150  TWO$ = MID$(X$,2,1)           ' Look at char after the dot.
160  TWO = ASC(TWO$)
170  IF TWO >= 160 AND TWO <= 175 THEN GOTO 210     ' It's ok.
180  IF TWO >= 32 AND TWO <= 47 THEN GOTO 210
190  X$ = MID$(X$,3)               ' Kill the char
200  GOTO 80
210  SIZ = LEN(X$)                 ' How much input was actual data
220  READIN = 65 - SIZ
230  XTWO$=INPUT$(READIN,#1)       ' Get rest of data
240  X$ = X$ + XTWO$ : X$ = LEFT$(X$,64)
250  PRINT X$         ' Optional - use this line to follow the transmission
260  GOSUB 290
270  PRINT#2,X$;      ' Put data to the file.
280  GOTO 60
290  ' Get two chars, subtract space (20 hex) from each, and combine
300  ' to one digit.
310  FOR A = 1 TO 32
320    Y$ = MID$(X$,A,1)
330    Z$ = MID$(X$,A+1,1)
340    YNUM = ASC(Y$) : ZNUM = ASC(Z$)
350    IF YNUM > 127 THEN YNUM = YNUM - 128    ' Turn off hi bit if on
360    IF ZNUM > 127 THEN ZNUM = ZNUM - 128
370    YNUM = YNUM -32 : ZNUM = ZNUM -32       ' Subtract the space
380    XNUM = (16 * YNUM) +ZNUM
390    NEWCHR$ = CHR$(XNUM)
400    X$ = MID$(X$,1,A-1) + NEWCHR$ + MID$(X$,A+2)
410  NEXT A
420  RETURN
430  PRINT  " [All done.]"
440  CLOSE #1,#2                            ' Clean up.
450  END

If  you already have a working Kermit on your PC and you want to get a new one,
you should use Kermit itself to transfer the KERMIT.FIX file.   Once  you  have
the new KERMIT.FIX on your PC disk:

   1. Rename KERMIT.EXE to something else, so you'll still have it in case

                                    - 45 -


      something goes wrong.

   2. Modify KGET:

         a. Remove lines 10 and 20.

         b. Change line 30 to 

                30   OPEN "KERMIT.FIX" FOR INPUT AS #1

         c. Remove line 60, since we're not handshaking with a remote host
            any more.

         d. In line 70, change "65" to "64".

         e. Remove  line 250, since there's no need to monitor a transmis-
            sion line.

         f. Change line 280 from "GOTO 60" to "GOTO 70".

   3. Save the modified KGET under a new name, say KEXE.BAS, and  run  it.
      It  will end with some error like "Input past end in 70", which just
      means it came to the end of file (of course, you  could  avoid  this
      error by trapping it, but no harm is done in any case).

   4. You  should now have a new, working version of KERMIT.EXE on your PC
      disk.