SLRNK+ 2.00 NOTES

:HEXNUM

	:HEXNUM may now refer to a global symbol that has been
defined.  For instance, /A:ABSEND may be used if ABSEND has already
been defined.

/E[:HEXNUM]

	/E may now take an optional start address.

FILENAME

	FILENAME may now be of the form [DU:]FILENAME[.EXT] where
D is A-P, U is user number 0-31, and .EXT is an extension overide.
If a colon is used a D and/or U must be given.  Very useful for
searching libraries from other user numbers.


                         Other Features

Standard console I/O now used so ^P works.

ZCPR3 Error flag is supported.

Fillvalue fills to end of last sector written.

Range output status line fixed/more informative.  The numbers in parens
are the first and (last address +1) used in this link.  The last number
is the number of bytes actually initialized and written.  I.E., if your
program ends with a DS array, that address space will show as used, but
not written out.

Error messages now appear in /V file.

/U works to a disk file.

The program start address and jump work on any page boundary, like /a:3,
not just /a:103.

For MP/M, virtual table file names are based on current bank #, so multiple
links will not conflict.  All REL files opened R/O.

SLRNK+ will search an alternate DU: if a file cannot be found where specified.
This includes the SLRNK-.MSG file if not under the default DU.


                         LNKFIG+ OPTIONS

MSDOS based emulation.  Certain optimizations are performed and/or not
performed based on this selection.

Keep Empty external chains.  This option selects whether or not SLRNK+ ignores
external reference tokens that are not referenced.  Some libraries require
this set, others generate more compact code if this is not set.

Kill console and detach.  This option is only available under MP/M.  If
selected, SLRNK+ will detach from the console and perform no console I/O.
In other words, you must give the complete command on the command line (easy
with /I).  SLRNK+ will become a background task with slightly reduced priority.

Optimize2.2.  Certain optimizations are performed if running under CP/M 2.2.
If you 2.2-compatible is not real close to CP/M, you will probably need to
disable this.

ERA $$$.SUB.  This selects whether or not SLRNK+ deletes the $$$.SUB file if
any errors are detected.  This will abort a submit file under 2.2.

Suppress 'Going Virtual'.  If you don't care when the internal tables start
overflowing to disk, disable this.

Virtual Drive.  When internal tables overflow, this says which drive to use.
Select the fastest drive available to use for virtual tables.

Alternate Drive. Alternate User.  This is where SLRNK+ will look for any file
not found where it should have been.