; * WARNING WARNING WARNING WARNING WARNING WARNING WARNING *

;   Please do not try to use external procedures
;   unless you are familiar with assembly language.
;
;   IMPORTANT: Externals must be written in assembly language.
;
;   The following example translates a string to upper case.

;
;   Place the following code in a file: "STU.ASM"
;


CODE    SEGMENT
        ASSUME     CS:CODE

STU     PROC       NEAR

        PUSH       BP                    ; SAVE ENVIRONMENT
        MOV        BP,SP                 ; MANUAL PAGE 189

        LES        DI,[BP+4]             ; GET PARAMETER
        MOV        CL,ES:[DI]
        INC        CL
L1:     DEC        CL
        JZ         L2
        INC        DI
        CMP        ES:BYTE PTR[DI],'a'
        JB         L1
        CMP        ES:BYTE PTR[DI],'z'
        JA         L1
        SUB        ES:BYTE PTR[DI],20H
        JMP        SHORT L1

L2:     MOV        SP,BP                 ; RESTORE ENVIRONMENT
        POP        BP                    ; MANUAL PAGE 190
        RET        4
STU     ENDP
CODE    ENDS
        END

; Now exit to PC-DOS and type:
;
; ASM STU
; LINK STU
; EXE2BIN STU.EXE STU.COM
;
; IGNORE MINOR ERRORS FROM ASM AND LINK



To use, write the following program:


type
  AnyString = string[255];

var
  S: AnyString;
  I: integer;


procedure STU(var S: AnyString); external 'STU.COM';

begin
  readln(S);
  STU(S);
  writeln(S);
end.




;   The above external procedure is only an example. You
;   can achieve the same result in Turbo-Pascal:
;
;   procedure STU(var S: AnyString);
;   var
;     I: integer;
;   begin
;     for I:=1 to Length(S) do S[I]:=Upcase(S[I]);
;   end;
;