NAME
        zmac - relocating Z-80 assembler

SYNOPSIS
        zmac  relfile,listfile=asmfile

DESCRIPTION

ZMAC is a Zilog mnemonic assembler with command and language
syntax similar to DEC assemblers. "relfile" is the object file
name, with the default extension ".OBJ" (for the format, see
OBJ.DOC). "listfile" is the listing file, with the default
extension ".PRN". In addition to standard disk files, you can
specify "LST:" for the list device or "CON:" for the console.
"asmfile" is the input assembly language file, with the default
extension ".ASM". The output files are both optional, so that

        zmac frodo=frodo

reads FRODO.ASM and creates FRODO.OBJ, while

        zmac ,frodo=frodo

creates only FRODO.PRN, and

        zmac frodo,frodo=frodo

creates both. Listing files are rarely needed except for final
documentation, since lines with syntax errors are automatically
listed to the console.

If ZMAC is called with no arguments, it will obey multiple
commands of the above format, prompting for each with "ZMAC>".
Operating this way saves time, since the assembler gets read in
only once. An empty command line terminates the input.


INPUT LANGUAGE

The language accepted by ZMAC is like that for the Zilog
assembler, with a few exceptions...

ZMAC does not require the "-$" after relative jump arguments.
The standard and ZMAC syntaxes are as follows:

standard:               JR      SOMEWHERE-$
ZMAC:                   JR      SOMEWHERE .

For equates, the syntaxes are:

standard:       BELL    EQU     7H
ZMAC:           BELL    =       7H .

A colon is forbidden after an equated symbol, but both a colon
and whitespace (space, tab, or carriage return) are required
after a label.

Symbols defined in the current module which are to be
referenced in other modules (exported symbols), or those
referenced in the current module but defined elsewhere
(imported symbols) must be declared GLOBAL:

                        GLOBAL  WARFARE

The ORG directive is illegal. There is instead the AORG
("absolute ORG") to set the program counter to a given absolute
address. The bad news is that ZLINK has a bug in its handling
of AORG. If one module has an AORG, then the NEXT module can't
correctly import symbols. The good news is that an AORG is
hardly ever necessary. ZLINK starts the code at 100H by
default. There is also an RORG ("relative ORG") directive,
which sets the program counter to a particular value with
respect to the module beginning.

Symbols and opcodes can be in either upper or lower case (no
case distinction). A symbol may have at least 100 characters,
and the first 16 characters are significant. In addition to the
standard alphabetic and numeric characters, the four characters
"_$.%" are also permitted in symbols. A "$" by itself stands
for the value of the program counter (the location of the first
byte in the CURRENT machine instruction). For example, an
infinite loop can be coded as "JP $".

Numbers should start with a numeral, which can be zero. By
default, the number is interpreted in decimal. The base of the
number can be set by a letter at the end of the number: D for
decimal, H for hex, O for octal, or B for binary.

The assembler can evaluate quite complex expressions.
Multiplication and division have higher precedence than
addition or subtraction (as usual for most software, but untrue
for the Zilog assembler). Parentheses are permitted to enforce
a certain evaluation order, but parentheses around an entire
expression denote indexing.

The unary operations are:       +    (no operation)
                                -    negate (2's complement)
                                #    1's complement

The binary operations are:      + - * / as usual
                                \       inclusive or
                                &       and

EXAMPLE

Consider the following assembly:

        C>zmac demo,demo=demo
        SSD RELOCATING   (AND EVENTUALLY MACRO)  Z80 ASSEMBLER VER 1.07

            0  ERRORS

...or the equivalent assembly using interactive input:

        C>zmac
        SSD RELOCATING   (AND EVENTUALLY MACRO)  Z80 ASSEMBLER VER 1.07
        ZMAC>demo,demo=demo


            0  ERRORS
        ZMAC>


            0  ERRORS TOTAL
        C>

The resulting listing file DEMO.PRN is as follows:

                                          PAGE NO.    1
                      1 ;Demonstration of ZMAC assembly language
                      2 ;syntax and resulting object code
                      3 ;
                      4 ;declare imported symbol before use
                      5         GLOBAL  OMICRON
                      6 ;declare exported symbol before definition
                      7         GLOBAL  ALPHA
                      8 ;
                      9 ;Equal sign rather than "EQU",
                     10 ;and colon is illegal
   0001=             11 ONE     =       1
                     12 ;using local symbol
  '0000  0700'       13         DW      SIGMA
                     14 ;lower case is synonymous
  '0002  0700'       15         dw      sigma
  '0004  0C00'       16         DW      MU
                     17 ;both colon and whitespace (blank, tab,

                     18 ;or CRLF) are required after label
  '0006: 00          19 ALPHA:  DB      0
  '0007:             20 SIGMA:
                     21 ;using "extended alphabet"
                     22 ;in symbol names
  '0007: 01          23 _BETA:  DB      1
  '0008: 0F          24 BE_TA:  DB      15
  '0009: 02          25 .GAMMA: DB      2
  '000A: 03          26 $DELTA: DB      3
  '000B: 04          27 %EPSILON: DB    4
                     28 ;       "EF" is optional
  '000C: 05          29 MU:     DEFB    5
  '000D: 0600        30 NU:     DEFW    6
                     31 ;
  '000F:             32 RHO:    DS      16
                     33 ;precedence used in
                     34 ;evaluating expressions
  '001F  07          35         DB      1+2*3
  '0020? 0000        36         DW      OMICRON
  '0022  88          37         DB      88H
                     38 ;single or double quotes around string
                     39 ;(double either to insert into string)
  '0023  4A6F6527    40         DB      'Joe''s mom'
  '002C  20226861    41         db      " ""hates"" chocolate"
  '003E? 00          42         DB      OMEGA
  '003F  88          43         DB      88H
                     44 ;declare exported symbol after definition
                     45         GLOBAL  RHO
                     46 ;declare imported symbol after use
                     47         GLOBAL  OMEGA
    0  ERRORS

                                          PAGE NO.    1

Addresses and data values subject to relocation are marked with
single quotes.  Imported values are marked with question marks.


FORMAT OF .OBJ FILE

The following information was gleaned from inspection of the
source code of the assembler and linker, and output generated
by the assembler. It didn't come from Bruce Mallett, so any
errors aren't his fault.                - Jim Van Zandt

The relocatable file created by ZMAC consists of a module
record, a series of data records, symbol records, and set
address records, and is terminated by an end of module record.


An end of module record has the format:

        DB      2,0


A module start record has the format:

LGH1:   DB      NEXT1-LGH1      ;# bytes in record
        DB      1               ;signals MODULE record
        DB      YY              ;descriptor bits (see below)
        DB      'FREEMONT'      ;optional module name
NEXT1:


A set address record is generated for each DEFS or DS opcode.
It has the effect of resetting the linker's program counter. It
has the format:

LGH2:   DB      NEXT2-LGH2      ;# bytes in record
        DB      2               ;signals SET ADDRESS record
        DB      YY              ;descriptor bits
        DW      XXXX            ;new value for program
;                               counter
NEXT2:


A data record has the following format:

LGH3:   DB      NEXT3-LGH3      ;# bytes in record
        DB      3               ;signals DATA record
        DS      28              ;one bit is set for each word
                                ;of data requiring relocation.
        DB      23,34,17,...,1BH ;1 to 224 bytes of data.
NEXT3:


A symbol record is used to import or export a global symbol. It
has the format:

LGH4:   DB      NEXT4-LGH4      ;# bytes in record
        DB      4               ;signals SYMBOL record
        DB      YY              ;descriptor bits
        DW      XXXX    ;if defined here, XXXX is the value of
;                       the symbol. If not defined here, XXXX
;                       is the  address requiring the symbol.
;                       The value of the symbol will be added
;                       to the word  at XXXX. In either case,
;                       if "relocatable",  then XXXX is with
;                       respect to the beginning  of the module.
        DB      'GANDOLF'       ;the symbol
NEXT4:

In the above records, the "descriptor bits" are defined as
follows:

        bit 0   if word rather than byte
        bit 1   if defined here
        bit 2   if global rather than local
        bit 3   if relocatable rather than absolute
        bit 4   if value of symbol is to be shifted left
                by 3 bits.

The "shift left 3 bits" note is used when the bit number in a
SET, BIT, or RES instruction is an imported symbol. In those
instructions, the bit number field is in bits 3 through 5 of a
byte. Note that it is always characteristic of a use, never a
definition, of a symbol.

The object code corresponding to the above assembly listing is:

C>dump demo.obj
DUMP version 00.05
        RECORD:  0
0000 0301 002D 03A8 0000-0000 0000 0000 0000  ...-.(..........
0010 0000 0000 0000 0000-0000 0000 0000 0000  ................
0020 0007 0007 000C 0000-010F 0203 0405 0600  ................
0030 0502 0A1F 000C 0405-2000 4F4D 4943 524F  ........ .OMICRO
0040 4E0A 0404 3E00 4F4D-4547 413F 0300 0000  N...>.OMEGA?....
0050 0000 0000 0000 0000-0000 0000 0000 0000  ................
0060 0000 0000 0000 0000-0007 0000 884A 6F65  .............Joe
0070 2773 206D 6F6D 2022-6861 7465 7322 2063  's mom "hates" c
        RECORD:  1
0080 686F 636F 6C61 7465-0088 0B04 0B0A 0024  hocolate.......$
0090 4445 4C54 4108 0402-0100 4F4E 4508 040F  DELTA.....ONE...
00A0 0F00 5248 4F0B 040B-0900 2E47 414D 4D41  ..RHO......GAMMA
00B0 0D04 0B0B 0025 4550-5349 4C4F 4E0A 040B  .....%EPSILON...
00C0 0700 5349 474D 410A-040F 0600 414C 5048  ..SIGMA.....ALPH
00D0 410A 040B 0800 4245-5F54 4107 040B 0C00  A.....BE_TA.....
00E0 4D55 0704 0B0D 004E-550A 040B 0700 5F42  MU.....NU....._B
00F0 4554 4102 0000 0000-0000 0000 0000 0000  ETA.............

The first byte of relocation bits in the first data record
(relative address 0005 in the file) is A8 hex, or 10101000
binary, signifying that words beginning at bytes 0, 2, and 4
among the following data bytes must be relocated. The last nine
bytes displayed are extraneous, since the end of module record
is at 00F3 and 00F4.

For more information, see the source files.


POTENTIAL IMPROVEMENTS

Handle multiple program counters, such as one each for "code",
"initialized data", and "uninitialized data".

Permit "EQU" as well as "=".

Make colons optional after either equated symbols or labels.

Make "ORG" a synonym for "AORG".


BUGS

A file name can't include a '-'.


AUTHOR
        Bruce Mallett