*  PROGRAM:  INUSE
*  AUTHOR:  RICHARD CONN
*  VERSION:  1.1
*  DATE:  6 MAR 82
*  DERIVATION:  From BANNER Version 1.0 by Richard Conn ... which was from:
*  DERIVATION:  From Public Domain BANNER Program, Author Unknown
*  PREVIOUS VERSIONS:  1.0 (12 Jan 82)
*
*********************************
*				*
*   I N U S E  P R I N T	*
*				*
*********************************
*
*  INUSE is a program which prints large (5x7) block letters
* on the CON: Device the word 'INUSE'.  When first started up, INUSE
* asks for a password, to which the user gives a desired password.
* INUSE is intended to be terminated by the user typing an Escape Character
* and then giving the original password.
*
*  INUSE is executed in one of three forms:
*	INUSE -- Normal operation
*	INUSE /C -- Print INUSE Banner and Return to CP/M (C is for Continue)
*	INUSE /? -- Prints HELP Info
	SHLD	START	; SAVE START OF STRING

*  INLINE RESTART LOOP
INL0:	LHLD	START	; GET START OF STRING
	MVI	C,0	; SET CHAR COUNT

*  MAIN LOOP
INL1:	CALL	CIN	; GET INPUT CHAR
	CPI	NULL	; DO NOT PERMIT <NULL>
	JZ	INL1
	CPI	BS	; BACKSPACE?
	JZ	INBS
	CPI	DEL	; DELETE?
	JZ	INDEL
	CPI	TAB	; TABULATE?
	JZ	INTAB
	CPI	CR	; CARRIAGE RETURN?
	JZ	INCR
	CPI	LF	; LINE FEED?
	JZ	INLF
	CPI	CTRLU	; CTRL-U?
	JZ	RESTRT
	CPI	CTRLX	; CTRL-X?
	JZ	REXSTRT
	CPI	CTRLR	; CTRL-R?
	JZ	RETYPE
	MOV	M,A	; STORE CHAR
	INX	H	; PT TO NEXT
	CALL	CTRL	; PRINT CHAR
	INR	C	; INCR CHAR CNT
	JMP	INL1

*
*  ** INLINE MODULES **
*
*  TAB -- TABULATE TO NEXT TAB STOP
INTAB:	MOV	M,A	; STORE <TAB>
	INX	H	; PT TO NEXT CHAR POSITION
	CALL	INTAB0	; TABULATE
	JMP	INL1

*  CTRL-R -- RETYPE CURRENT LINE
RETYPE:	MVI	M,0	; STORE END OF STRING CHAR
	MVI	C,0	; RESET CHAR CNT
	LHLD	START	; GET START ADDRESS
	CALL	HASH	; PRINT HASH CHAR
RETY1:	MOV	A,M	; GET CHAR
	ORA	A	; ZERO?
	JZ	INL1	; CONTINUE
	CALL	CTRL	; PRINT IT
	MOV	A,M	; GET CHAR AGAIN
	CPI	TAB	; DON'T COUNT IF <TAB>
	JZ	RETY2
	CPI	BEL	; DON'T COUNT IF <BEL>
	JZ	RETY2
	INR	C	; INCR CHAR CNT
RETY2:	INX	H	; PT TO NEXT CHAR
	JMP	RETY1

*  CTRL-U -- ERASE LINE AND RESTART
RESTRT:	CALL	HASH	; PRINT HASH CHAR
	JMP	INL0	; START UP AGAIN

*  CTRL-X -- ERASE (AND BACKSPACE) LINE AND RESTART
REXSTRT:
	MOV	A,C	; CHECK FOR EMPTY LINE
	ORA	A	; 0 CHARS?
	JZ	INL0
	CALL	EXBS	; <BS>
	JMP	REXSTRT

*  LINE FEED -- INSERT <CR> <LF> AND ECHO <CR> <LF>
INLF:	MVI	M,CR	; STORE <CR>
	INX	H	; PT TO NEXT
	MVI	M,LF	; STORE <LF>
	INX	H	; PT TO NEXT
	MVI	C,0	; RESET CHAR CNT
	CALL	CRLF	; NEW LINE
	JMP	INL1

*  DELETE -- DELETE PREVIOUS CHAR AND ECHO DELETED CHAR
INDEL:	CALL	BOL	; BEGINNING OF LINE?
	JZ	INL1	; CONTINUE
	DCX	H	; BACK UP
	MOV	A,M	; GET CHAR
	CALL	CTRL	; PRINT CHAR
	CPI	BEL	; DON'T CHANGE COUNT IF <BEL>
	JZ	INL1
	INR	C	; INCR DISPLAY CHAR COUNT
	JMP	INL1

*  BACKSPACE -- DELETE PREVIOUS CHAR AND BACK UP CURSOR
INBS:	CALL	EXBS	; EXECUTE <BS>
	JMP	INL1

*  BACKSPACE ROUTINE
EXBS:	CALL	BOL	; BEGINNING OF LINE?
	RZ		; CONTINUE IF SO
	DCR	C	; DECR COUNT
	DCX	H	; BACK UP
	MVI	A,BS	; PRINT <BS>
	CALL	COUT
	MVI	A,' '	; <SP>
	CALL	COUT
	MVI	A,BS	; <BS>
	CALL	COUT
	RET

*  CARRIAGE RETURN -- DONE; STORE ENDING ZERO
INCR:	MVI	M,0	; STORE ENDING ZERO
	CALL	CRLF	; NEW LINE
	POP	PSW	; RESTORE PSW
	POP	B	; RESTORE REGS
	POP	D
	POP	H
	RET

*
*  ** SUPPORT ROUTINES **
*  BOL -- RETURNS W/ZERO FLAG SET IF USER AT BEGINNING OF LINE
*
BOL:	XCHG		; DE=HL
	LHLD	START	; GET START ADR
	XCHG		; HL RESTORED
	MOV	A,D	; CHECK FOR MATCH
	CMP	H	; MATCH?
	RNZ		; NO MATCH
	MOV	A,E	; CHECK FOR COMPLETE MATCH
	CMP	L
	RNZ		; NO MATCH
	PUSH	PSW	; SAVE FLAGS
	MVI	A,BEL	; BEEP
	CALL	COUT
	POP	PSW
	RET

*  CTRL -- IF CHAR>=<SP>, PRINT IT; OTHERWISE, PRINT AS CTRL-CHAR
CTRL:	CPI	' '	; <SP>?
	JC	CTRL1
	JMP	COUT	; PRINT IT NORMALLY
CTRL1:	CPI	TAB	; TRAP <TAB>
	JZ	INTAB0
	JMP	COUT	; PRINT

*  HASH -- PRINT HASH MARK FOLLOWED BY <CR> <LF>
HASH:	MVI	A,'#'	; PRINT HASH CHAR
	CALL	COUT
	JMP	CRLF

*  INTAB0 -- TABULATE ON SCREEN
INTAB0:	MOV	A,C	; GET CHAR CNT
	ANI	7	; MASK FOR DIFFERENCE FROM 8
	MOV	B,A	; STORE IN REG B TEMPORARILY
	MVI	A,8	; SUBTRACT FROM 8
	SUB	B
	MOV	B,A	; <SP> COUNT IN B
	ADD	C	; ADD TO CHAR COUNT
	MOV	C,A
	MVI	A,' '	; <SP> IN A
INTAB1:	CALL	COUT	; PRINT <SP>
	DCR	B	; COUNT DOWN
	JNZ	INTAB1
	RET
*
*  CHARACTER TABLE
*    THE CHARACTERS REPRESENTED IN THIS TABLE ARE IN A 5X7 FORMAT
*    THE FIRST BYTE IN EACH ENTRY REPRESENTS THE FIRST CHAR TO PRINT, ETC
*    THE BITS 6 TO 0 REPRESENT LINES (SUCCESSIVE) TO PRINT FOR THE CHAR
*
CHARS:
	DB	00H,00H,00H,00H,00H	;<SP>
	DB	00H,00H,7DH,00H,00H	;EXCLAMATION MARK
	DB	00H,70H,00H,70H,00H	;"
	DB	14H,7FH,14H,7FH,14H	;#
	DB	12H,2AH,7FH,2AH,24H	;$
	DB	62H,64H,08H,13H,23H	;%
	DB	36H,49H,35H,02H,05H	;&
	DB	00H,00H,70H,00H,00H	;'
	DB	1CH,22H,41H,00H,00H	;(
	DB	00H,00H,41H,22H,1CH	;)
	DB	22H,14H,7FH,14H,22H	;*
	DB	08H,08H,3EH,08H,08H	;+
	DB	00H,01H,06H,00H,00H	;,
	DB	08H,08H,08H,08H,08H	;-
	DB	00H,03H,03H,00H,00H	;.
	DB	02H,04H,08H,10H,20H	;/
	DB	3EH,45H,49H,51H,3EH	;0
	DB	11H,31H,7FH,01H,01H	;1
	DB	21H,43H,45H,49H,31H	;2
	DB	22H,41H,49H,49H,36H	;3
	DB	0CH,14H,24H,7FH,04H	;4
	DB	7AH,49H,49H,49H,46H	;5
	DB	3EH,49H,49H,49H,26H	;6
	DB	43H,44H,48H,50H,60H	;7
	DB	36H,49H,49H,49H,36H	;8
	DB	30H,49H,49H,49H,3EH	;9
	DB	00H,00H,36H,00H,00H	;:
	DB	00H,01H,16H,00H,00H	;;
	DB	08H,14H,22H,41H,00H	;<
	DB	14H,14H,14H,14H,14H	;=
	DB	00H,41H,22H,14H,08H	;>
	DB	20H,40H,4DH,50H,20H	;?
	DB	7EH,41H,5DH,4DH,39H	;@
	DB	3FH,48H,48H,48H,3FH	;A
	DB	7FH,49H,49H,49H,36H	;B
	DB	7FH,41H,41H,41H,41H	;C
	DB	7FH,41H,41H,41H,3EH	;D
	DB	7FH,49H,49H,49H,41H	;E
	DB	7FH,48H,48H,48H,40H	;F
	DB	7FH,41H,41H,49H,4FH	;G
	DB	7FH,08H,08H,08H,7FH	;H
	DB	41H,7FH,41H,80H,80H	;I
	DB	03H,01H,01H,01H,7FH	;J
	DB	7FH,08H,14H,22H,41H	;K
	DB	7FH,01H,01H,01H,01H	;L
	DB	7FH,20H,10H,20H,7FH	;M
	DB	7FH,30H,08H,06H,7FH	;N
	DB	7FH,41H,41H,41H,7FH	;O
	DB	7FH,48H,48H,48H,78H	;P
	DB	7FH,41H,45H,43H,7FH	;Q
	DB	7FH,48H,4CH,4AH,79H	;R
	DB	32H,49H,49H,49H,26H	;S
	DB	40H,40H,7FH,40H,40H	;T
	DB	7FH,01H,01H,01H,7FH	;U
	DB	70H,0CH,03H,0CH,70H	;V
	DB	7FH,02H,04H,02H,7FH	;W
	DB	63H,14H,08H,14H,63H	;X
	DB	60H,10H,0FH,10H,60H	;Y
	DB	43H,45H,49H,51H,61H	;Z
	DB	7FH,41H,41H,41H,00H	;[
	DB	20H,10H,08H,04H,02H	;\
	DB	00H,41H,41H,41H,7FH	;]
	DB	04H,08H,10H,08H,04H	;^
	DB	01H,01H,01H,01H,01H	;_
	DB	00H,40H,20H,10H,00H	;@
	DB	3FH,48H,48H,48H,3FH	;A
	DB	7FH,49H,49H,49H,36H	;B
	DB	7FH,41H,41H,41H,41H	;C
	DB	7FH,41H,41H,41H,3EH	;D
	DB	7FH,49H,49H,49H,41H	;E
	DB	7FH,48H,48H,48H,40H	;F
	DB	7FH,41H,41H,49H,4FH	;G
	DB	7FH,08H,08H,08H,7FH	;H
	DB	41H,7FH,41H,80H,80H	;I
	DB	03H,01H,01H,01H,7FH	;J
	DB	7FH,08H,14H,22H,41H	;K
	DB	7FH,01H,01H,01H,01H	;L
	DB	7FH,20H,10H,20H,7FH	;M
	DB	7FH,30H,08H,06H,7FH	;N
	DB	7FH,41H,41H,41H,7FH	;O
	DB	7FH,48H,48H,48H,78H	;P
	DB	7FH,41H,45H,43H,7FH	;Q
	DB	7FH,48H,4CH,4AH,79H	;R
	DB	32H,49H,49H,49H,26H	;S
	DB	40H,40H,7FH,40H,40H	;T
	DB	7FH,01H,01H,01H,7FH	;U
	DB	70H,0CH,03H,0CH,70H	;V
	DB	7FH,02H,04H,02H,7FH	;W
	DB	63H,14H,08H,14H,63H	;X
	DB	60H,10H,0FH,10H,60H	;Y
	DB	43H,45H,49H,51H,61H	;Z

*
*  BUFFERS
*
	DS	40	;20-ELT STACK
STACK:
	DS	2	;TOP OF BANNER STACK; CP/M STACK
CONTFLG:
	DS	1	;0=DON'T CONTINUE, 'C'=CONTINUE
START:
	DS	2	;START ADDRESS OF INPUT STRING
NEXTCH:
	DS	2
LLEN	EQU	80	;NUMBER OF CHARS IN LINE, MAX
INLINE:
	DB	LLEN	;CHAR COUNT FOR INLINE
	DS	LLEN+1
RDLINE:
	DB	LLEN	;CHAR COUNT FOR RDLINE
	DS	LLEN+1
COMMENT:
	DB	LLEN
	DS	LLEN+1
BLINE:
	DB	'* INUSE *',0	; MESSAGE

	END