H E A T H   E S C A P E   S E Q U E N C E S
        - - - - -   - - - - - -   - - - - - - - - -
  		typed by F.B.Ghofulpo
		   1979 August 26


C U R S O R   F U N C T I O N S

Sequence	Mnemonic	Definition
--------	--------	----------

ESC H		HCUH		Cursor Home
ESC C		HCUF		Cursor Forward
ESC D		HCUB		Cursor Forward
ESC B		HCUD		Cursor Down
ESC A		HCUU		Cursor Up
ESC I		HRI		Reverse Index
ESC n		HCPR		Cursor Position Report
ESC j		HSCP		Save Cursor Position
ESC k		HRCP		Set Cursor to Previously Saved Position
ESC Y		HDCA		Direct Cursor Addressing (VT52)



E R A S I N G   A N D   E D I T I N G

ESC E		HCD		Clear Display (Shift Erase)
ESC b		HBD		Erase Beginning of Display
ESC J		HEOP		Erase to End of Page (Erase Key)
Esc l		HEL		Erase Entire Line
ESC o		HEBL		Erase Beginning of Line
ESC K		HEOL		Erase to End of Line
ESC L		HIL		Insert Line
ESC M		HDL		Delete Line
ESC N		HDCH		Delete Character
ESC @		HEIM		Enter Insert 
ESC O		HERM		Exit Insert Character Mode



C O N F I G U R A T I O N

ESC z		HRAM		Reset to Power-Up Configuration
ESC r Bn	HMBR		Modify Baud Rate (Bn=; A=110, B=150,
				  C=300, D=600, E=1200, F=1800, G=2000,
				  H=2400, I=3600, J=4800, K=7200, L=9600)
				 (M=19200 Should for dumb terminal use.)

ESC x Ps	HSM		Set Mode(s): Ps=
				  1 = Enable 25th line
				  2 = No key click
				  3 = Hold screen mode
				  4 = Block cursor
				  5 = Cursor off
				  6 = Keypad shifted
				  7 = Alternate keypad mode
				  8 = Auto line feed on CR
				  9 = Auto CR on line feed

ESC y Ps	HRM		Reset mode(s): Ps=
				  1 = Disable 25th line
				  2 = Enable key click
				  3 = Exit hold screen mode
				  4 = Underscore cursor
				  5 = Cursor on
				  6 = Keypad unshifted
				  7 = Exit alternate keypad mode
				  8 = No auto line feed
				  9 = No auto CR

ESC <		HEAM		Enter ANSI Mode



M O D E S   O F   O P E R A T I O N

ESC [		HEHS		Enter Hold Screen Mode
ESC \		HXHS		Exit Hold Screen Mode

ESC p		HERV		Enter Reverse Vidio Mode
ESC q		HXRV		Exit Reverse Vidio Mode

ESC F		HEGM		Enter Graphics Mode
ESC G		HXGM		Exit Graphics Mode

ESC t		HEKS		Enter Keypad Shifted Mode
ESC u		HXKS		Exit Keypad Shifted Mode

ESC =		HAKM		Enter Alternare Keypad Mode
ESC >		HXAM		Exit Alternate Keypad Mode



A D D I T I O N A L   F U N C T I O N S

ESC }		HDK		Keyboard Disable
ESC {		HEK		Keyboard Enable
ESC v		HEWA		Wrap Around at End of Line
ESC w		HXWA		Discard at End of Line
ESC Z		HID		Identify as VT52 (ESC / K)
ESC ]		HX25		Transmit 25th Line
ESC #		HXMP		Transmit Page

Note: The Terminal will transmit the following sequences, but 
it will not respond to them if they are received by the Terminal.

ESC S		HF1		Function Key #1 (f1)
ESC T		HF2		Function Key #2 (f2)
ESC U		HF3		Function Key #3 (f3)
ESC V		HF4		Function Key #4 (f4)
ESC W		HF5		Function Key #5 (f5)
ESC P		HF7		Function Key #7 (BLUE)
ESC Q		HF8		Function Key #8 (RED)
ESC R		HF9		Function Key #9 (GRAY)


---------
E N D