NEWTERM for the EPSON PX-8
                   --------------------------

This  program is a versatile terminal emulator specially  written 
for  the  Epson PX-8.  It assumes that you are  working  with  an 
external  RAM-disk;  or at least that you have <2k internal  RAM-
disk (Set this with Config).  Among other possibilities,  NEWTERM 
enables you to send and receive files using the XMODEM  protocol. 
This protocol divides your files up into blocks of 128 bytes, and 
sends these one by one,  waiting for an acknowledgement of proper 
reception each time, before sending the next block.

              NEWTERM features the following modes:

- Dumb terminal emulation;
  Which is not, in fact, so dumb, because it allows you to select 
  a number of possibilities regarding character echo and linefeed 
  insertion.  It  is  transparent  for  all  characters  (1-255), 
  excluding Null.  Also, before connecting you, the program tells 
  you  if you have not connected the RS-232 port properly (or  if 
  the other side is switched off).  Note,  however, that the only 
  criterion for the PX-8 to send or 'hang' is 'pin 5', Cleared to 
  Send (CTS).  Or CT106, Ready for Sending, if you are CCITT- and 
  V24-minded!
  NEWTERM  does  not support Xon/Xoff unless this  is  set  while 
  selecting  the operating mode of the RS-232 port (By a machine-
  language  procedure or with BASIC).  Of course,  when the  PX-8 
  works in Xon/Xoff mode,  NEWTERM is not transparent for the Xon 
  and Xoff characters!

- Dumb download (receive) mode;
  This  is  a VERY useful mode,  which enables  you  to  receive, 
  without  protocol,  any  file (up to 42 kByte) via  the  RS-232 
  port. You terminate file transfer by pressing any key locally.
  With this mode you can,  for instance,  finally receive a .COM-
  file which another computer is PIPping to you.  Previously, the 
  only  way,  at  least for .COM-files and any other files  which 
  contain CTRL-Z and the like,  was to put it on a disk or micro-
  cassette and transfer this!
  Because  no protocol is used,  reception speed is  limited.  To 
  enable you to see if a file has been received properly, NEWTERM 
  displays  the number of bytes received.  In any case,  you will 
  find that transfer at speeds over 1200 BPS is unreliable.

- Dumb Upload (Send) mode;
  To send any file without protocol.

- XMODEM upload;
  Which enables you to send files (Again, of any type) to another 
  computer,  using  the  famous Ward Christensen 'XMODEM'  error-
  correcting  protocol.  You  can send files at any  speed  - the 
  protocol will take care that everything arrives properly.  This 
  protocol  is used on most 'bulletin-boards'.  NEWTERM uses  the 
  version with Checksum error-check (i.e.  not CRC),  as this  is 
  the original, and most common version.

- XMODEM Download;
  This mode,  finally, enables you to receive any file (Up to 42k 
  in  size)  again using the same XMODEM protocol.  The 42k  size 
  limitation  is due to the fact that any file received is  first 
  stored in an array in memory before being saved to disk  - this 
  to prevent very frequent disk accesses.

                        Operating NEWTERM

Because  NEWTERM is menu-driven and always tells you exactly what 
you can or must do,  it is self-explanatory. Please note that the 
XMODEM  upload- and download-modes time out automatically if  the 
RS-232 port is connected but no activity is detected on the other 
side.  Also note that to leave the Terminal mode,  you must press 
HELP.


-----------------------------------------------------------------
Comments, suggestions for Improvements, etc., to the author:
     
          Michael V. Willems BSc(Eng)
          Onderwei 1
          1273 TA  Huizen
          the Netherlands.  tel. +31 2152 62734

The source listing (in Turbo-Pascal) is available upon request.
-----------------------------------------------------------------