HOW TO PRINT PORTABLE WORDSTAR FILES TO UNSUPPORTED  
                         PRINTERS WITH THE GENEVA PX/8
         
         Portable WordStar is configured for an Epson RX or FX 
         printer.  When printing Portable WordStar files to a printer 
         other than an Epson RX or FX, the printout may not be 
         formatted as desired because of conflicting or unrecognized 
         printer codes used by WordStar.  The file may be printed with 
         incorrect line spacing, some unwanted characters may be 
         printed, or it may be printed in a typestyle other than one 
         you prefer.  These problems can be overcome by PIPing the 
         file to the list device.  The following is a description of 
         this procedure:  
         
         After you have created a file, store it as you normally 
         would and go back to the "Opening Menu".  Select "P" for 
         PRINT a file.  Provide the name of the file to print when 
         prompted.  WordStar will then display: 
              DRIVE FILE OUTPUT (Y/N): <enter Y for Yes>
               OUTPUT FILE NAME? <supply a file name>
              <answer the other print questions accordingly>
                  This will create a file on disk formatted for
         printing.  Exit WordStar to CP/M.  At the prompt, enter 
         "PIP LST:=Filename[Z]" (where Filename is the name of the 
         output file created from the WordStar print routine).  Enter 
         a Z in square brackets after the file name, so PIP will strip 
         the eighth bit.  The [Z] may not be required on all printers, 
         but if you were not to use it on an Epson printer, the last 
         character in each word would be printed in italics.
           
         
                  SENDING CONTROL CODES TO AN UNSUPPORTED PRINTER 
                            FROM PORTABLE WORDSTAR
         
         Using a procedure similar to the one described above, you can 
         send certain control codes to your printer using Portable 
         WordStar.  If you create a file in WordStar, you can embed an 
         Escape code by typing CTRL P, then ESC, then the code.  For 
         example, on the Epson LQ-1500 or an Epson printer with an NLQ 
         board, to turn on Letter quality, you would enter
            CTRL P ESC x 1  (no spaces between keystrokes).
         This will get embeded in the file, but will not print in a 
         file that has been formatted for printing through the 
         WordStar print routine.  You can print a file with an embeded 
         Escape code if the file is saved (rather than printed) to 
         disk, but it will not be properly formatted.  If you need an 
         Escape code to access a particular feature of your printer 
         you could create a file that consists only of the Escape 
         code, store it to disk, PIP it to the printer, then PIP your 
         formatted file to the printer.  The following is an example 
         of how to print a Portable WordStar file to an NLQ Board in 
         Letter Quality.  (In this example, the files are stored on 
         drive A and PIP is in drive C.)
         
         Create a file called "A:LQON.DOC" in WordStar.  In that file, 
         enter CTRL P ESC x 1 (type a "P" while holding the Control 
         key, press the ESC key, type an "x", then a "1" without 
         spacing between characters).  Save this file.  Create a file 
         that will contain the text you want to print and call it 
         "A:TEXT.DOC".  When you have finished that file, "Print" it 
         to disk using the output file name "A:TEXT.PRT" (the 
         extention ".PRT" is recommended so you know that this file 
         has been formatted for printing).  Exit WordStar to CP/M.  
         Enter the following at the prompt:
            C:PIP LST:=A:LQON.DOC
         wait for the prompt, then type:
            C:PIP LST:=A:TEXT.PRT[Z]
         
         You can select a different color on the JX-80 using this 
         procedure.  For example, for printing in Orange, you would 
         create a WordStar file with CTRL P ESC r 5, then PIP it to 
         the printer as described above.
         
         
         The idea for PIPing WordStar files to the list device is from 
         THE EPSON CONNECTION:  APPLE by Darnall and Corner.
         
         Richard Rockwell, Epson Mid Atlantic, November 1984
         
         eof.