Batteries for the PX-8
Roger P. McConochie
1-313-995-3452

        The single item which every PX user will eventually
require is a replacement battery pack.  In meeting this
need, users have a choice among at least three options.

        (1)  First, a user might choose to purchase the
genuine Epson item.  These battery packs (Epson RB 201,
#Y203-503-000), still being imported from Japan by Epson
America, are available from Computer Laboratories, in
Minnesota, at 1-800-888-9062.  The price is about $70.
They also offer a full range of PX (and QX-10/16) repairs.

        (2)  The second option is to purchase an "Epson-
equivalent" battery pack.  These are offered for $35
(plus S & H) from SnyderScope International, 111 South
Marshall, Suite 202, El Cajon, CA 92020 (1-619-442-2299).
For their eight-page catalog of QX and PX items (computers,
peripherals, accessories, parts, software, and supplies),
users are invited to send a self-addressed, double-stamped
($.45) envelope.  They present themselves as a small-scale,
friendly, informal organization: users do well to expect to
wait a month to receive the catalog and another month to
receive items which have been ordered.

        (3)  A third alternative is for users to have
replacement battery packs assembled by a local hobby shop
(or, for users handy with a soldering iron, to build their
own), at a cost of $13-35.

        The heart of such a pack is a set of four "sub-C"
size, standard-charge, tabbed, 1.2V 1100mAh nicad
batteries.  Hobby shops sell the Sanyo N-1200-SC cells for
about $6 each, whereas Radio Shack offers an equivalent
battery for $5.99 per package of two (#23-190).  Note
that, although "fast-charge" nicads (such as the Sanyo
"N-1200-SCR" cells) are available, they offer little
advantage.  While they might be more durable, they could
not be charged more quickly than the standard batteries:
although the PX adapter is rated at 600 mAh, a resistor
within the PX prevents the batteries from being charged
faster than the standard-charge rate for the Epson nicads
(150-200 mAh, with a 330 mAh maximum).

        Following the model provided by the Epson battery
pack, the new unit should be assembled by soldering
together (in series) the four batteries.  At the lower end,
the connection should be made using insulated wire (rather
than the uninsulated tabs or a section of bare wire), to
avoid having the batteries short out when jammed into the
battery compartment of the PX.  Because replacement packs
(with soldered connections) are likely to be slightly
longer than the Epson units (with their welded joints),
users may care to create another 1/8th-inch of space in the
battery compartment by removing the plastic piece at the
end of the compartment, using a utility knife to smooth out
the rough edges which remain.

        Because the battery connector is Epson-specific,
the user may care to cut the Epson leads in half, adding
a standard connector (with the female connector on the
battery leads, to minimize the chance of shorting out the
battery).  Note that only the smallest of connectors will
fit into the battery compartment of the PX-8.  The user
might choose a "dean pin" or, at a slightly greater cost,
a pin with distinct positive and negative leads, so that--
as with the Epson connector--it would be impossible to plug
in the battery incorrectly.  Following this procedure, new
battery packs could be made, using leads and the standard
connector, which could be swapped with other battery packs
as necessary.  The pack could then be finished off by
taping the batteries together, taping over both ends of the
pack, and then enclosing the four batteries in new "shrink
wrap."