MCTUTY: MICROCASSETTE TAPE UTILITY PROGRAM VERSION 0.8


           This paper covers the functions of the MCTUTY (MicroCassette 
      Tape  UTIlity) Program,  version 0.8,  for the Epson PX-8 & HX-40 
      computers.     The program provides 5 basic utility functions for 
      use with microcassettes:

      1) VERIFY:
           Test all the blocks and count the number of errors found.

      2) DIRECTORY:
           Recover and correct a tape directory that was garbaged.

      3) CONDENSE:
           Move  files stored at the back of a tape to the front  of  a 
      tape where all the open areas are.

      4) DUMP:
           Display data stored on a tape in HEX format.

      5) RECOVER:
           Read data from a tape and copy it to another storage device.  
      Any "bad" blocks are skipped over and the copying continues.


      *** PLEASE NOTE ***

           Practice  using this program using a "junk" tape with  dummy 
      files BEFORE you try it on the real thing.

           NEVER run this program without the AC Adapter CONNECTED.

           Play  it  safe,  ALWAYS copy all your files in RAM  Disk  to 
      Floppy  Disk  or Tape and remember to use the system function  to 
      REMOVE said backup tape.


      STARTING THE PROGRAM:

           Before  running the program,  enter the system menu and make 
      sure that the microcassette is not mounted.   Once done, exit the 
      system screen and select MCTUTY through the main MENU program  or 
      by typing "MCTUTY<RETURN>" at the CP/M level.

           There are 2 keys that have special functions: STOP & ESC.

      STOP  will  return the program to the main menu;  however if  the 
      program is in the main menu, STOP will cause the program to exit.

      ESC will return the program to the previous menu.

           These keys may be used at any time to move backward from the 
      current menu to an earlier menu.  Also, at any point in any menu, 
      CTRL-P may be used to obtain a hard copy of what you're doing.

           Once  in the main menu,  the number 1 - 5 may be entered  to 
      select a given function.  Pressing the RETURN Key is not required 
      to  select  a  function.   Use  of each function  is  covered  as 
      follows:


      (1)  VERIFY:

           Verify is used to test data stored on a tape.  VERIFY allows 
      for a selection of:

                1    Single File (Selectable)
                2    All Files (Until CTRL-STOP is pressed)

           Just press the number of the selection needed.

           If  "1" is pressed,  the program will read the directory  at 
      the  start  of the tape and display a menu of files that  may  be 
      verified.   Just  type  the number of the file that needs  to  be 
      tested  and then press the RETURN Key.   If more that one file is 
      to  be verified,  more than one number may be entered like  this, 
      "1,3,5,7".

           If "2" is pressed, the program will wind to the start of the 
      tape  and  test every file it finds until CTRL-STOP  is  pressed.  
      This  function does NOT stop running the cassette when the end of 
      the tape is reached.

           In both cases the information displayed is as follows:

                FileName.Ext    HDR    00000    EOF Error=00000
                ^               ^      ^        ^         ^
                |               |      |        |         |
                file name       header current  End       Total
                of file         was    block    Of        Errors
                                found  number   File      Found


      (2)  DIRECTORY:

           This  function is designed to restore a tape directory  that 
      was  garbaged  for some reason.   The recreation of  the  correct 
      directory may be done from the beginning or after a selected file 
      to the end of the tape or wherever you wish to stop.

                1    From Some File
                2    All Files

           If  "1" is entered,  the program will read the directory  at 
      the start of the tape,  then display a list a files that would be 
      the  starting point.   The starting point would be after the file 
      selected.   From  that  point on,  the program  will  update  the 
      directory based on what is found on tape.   Use CTRL-STOP to tell 
      the program that there are no more files to be found.

           If  "2" is entered,  the program will search for files  from 
      the  start  of the tape.   The function of the search is like  #1 
      above.   Use CTRL-STOP to tell the program that there are no more 
      files to be found.

           After  the search for files is finished,  the user is  given 
      the  option  of renaming any of the file  names.   This  function 
      exists because the same file name may exist on the tape more than 
      once.  In order to rename a file, just enter:

                number=filename.ext<RETURN>
                1=MYFILE.DOC

           A few words of warning about known bugs in this function:

           The record count of a recovered file will be 4 or 5  records 
      higher  than  what  it really is.   While this  doesn't  cause  a 
      problem  for text files that mark the end of file with a  CTRL-Z, 
      reading other files may be a problem,  if you try to pull a  copy 
      of  the  file  from tape.   The RECOVER Function can be  used  to 
      correct this problem and read the file correctly.

           This  function  does  not  seem to test  for  end  of  tape.  
      Therefore,  you should watch for the end of a tape or the program 
      will cause the tape drive to keep running and running EVEN AT THE 
      END OF A TAPE.

           The  RENAME part of the DIRECTORY Function does NOT  convert 
      lower case to upper case.   Thus, you could create a file name in 
      lower case that can NOT be recovered.  ALWAYS enter file names in 
      upper case.


      (3)  CONDENSE:

           If  you  must use this function,  please use this  one  with 
      care.   It  is possible to kill all the files on the tape and not 
      have  a way to recover any of them.   Once the red  record  light 
      comes on (or on then off),  DO NOT STOP this function or you will 
      lose your files.   Once started,  the function could take as long 
      as 45 minutes to do one side of a 30 minute tape.


      (4)  DUMP:

           The  DUMP  function allows a user to examine  the  data  and 
      header  information stored onto a tape.   This function allows  2 
      options:

                1    Single File (Selectable)
                2    All Files

           If  "1" is entered,  the tape directory will be read and the 
      file or files to be dumped are selected by number.  More than one 
      file is selected like this,  "2,4,6,8".   The program will return 
      to the file selection menu when finished dumping out the file(s).

           If  "2" is selected,  the program will wind the tape to  the 
      beginning and dump out what's stored from that point on.

           There are 2 known problems with this function:

           Like the RECOVER function,  this function does NOT test  for 
      the end of a tape.   Thus,  unless stopped by CTRL-STOP,  the the 
      program would keep the tape drive running on and on,  even at the 
      end of a tape.

           The  normal CTRL-S (PAUSE) does NOT halt a display  listing.  
      If  you  want to look over all the data,  use CTRL-P to send  the 
      data to the printer.

      The format of the data is as follows:
      (All numbers are in HEX)
           
           Block beginning tape count = HH HH <--- this is the value of
                                                   the tape counter at
                                                   the start of the
                                                   block.
           Block discrimination field = H1 H2 H3 H4

                H1 = The type of block:  48H = Header Block
                                         44H = Data Block
                                         45H = EOF Block

             H2 H3 = The Block Number (0000H - FFFFH)

                H4 = Block Copy Number:  00H = First Copy
                                         01H = Second Copy

                This information is followed by 256 hex bytes of data.



      (5)  RECOVER:

           This function copies files from the microcassette to another 
      storage device.   Any errors, such as bad blocks, are ignored and 
      256 bytes of spaces are returned for this type of error.  Errors, 
      such  as the wrong number of records in the header,  are  ignored 
      and  only the correct number of legal records are  copied.   This 
      function offers 2 options to recover:

                1    Single File
                2    All Files

           If "1" is selected, the tape directory is read and a menu of 
      possible files to be recovered is displayed.  A file is  selected 
      by  typing the number and a return.   The program will ask  where 
      the  file is to be copied to.   You can NOT copy a file from  the 
      microcassette  to the microcassette,  please do not select  drive 
      "H:"  as the destination drive.   Other files may be  copied,  by 
      waiting  for  this copy process to finish and entering in  a  new 
      number.

           If "2" is selected,  every block on the tape will be  copied 
      into  one  master  file.   Like option #1 above,  the  drive  and 
      filename  of the file to copy to is selected by the  user.   Also 
      drive "H:" can't be used as the destination drive.   I'm not sure 
      why this option exists,  because all the blocks on a  tape,  even 
      the  directory,  are  stored  on one large  unuseable  file.   In 
      theory,  one could use DUMP or DDT to look at all the blocks, but 
      users  will have problems understanding where one file  ends  and 
      the other begins.

           There are a few known bugs with this function:

           The file name selection does not convert lower case input to 
      upper  case.   Therefore,  it is possible to enter a output  file 
      name in lower case and CP/M would not be able to read it.  Always 
      enter all file names in upper case.

           When  option #2 is selected,  the program does NOT test  for 
      the end of a tape.   Thus, unless you enter CTRL-STOP to tell the 
      program  to stop copying,  the program will keep running the tape 
      drive even after the end of the tape is reached.









                                 DISCLAIMER:

           This software is given out AS IS and Epson shall not be held 
      liable for any damages,  direct or indirect,  caused through  the 
      use  of this program or the information contained in this  paper.  
      Because  the software is given out as is to end users,  Epson  is 
      not  required  in any way to support or provide updates  to  this 
      software.

           After testing the program for a few days,  it is clear to me 
      that  there  are several bugs within the  program.   While  every 
      effort has been made to find as many bugs as possible, it is very 
      likely  that  there are other unfound bugs within this  software.  
      This  program  was written by Epson Japan and given out by  Epson 
      America  to end users for free.   This program may be  copied  by 
      anyone  PROVIDED  that  the software is copied  on  a  NON-PROFIT 
      bases.   Epson  America  does  NOT have the source code  to  this 
      program.  

e is copied  on  a  NON-PROFIT 
      ba