To:     All MS OEMS
From:   JCP MS 8087 Software Engineering
RE:     OEM specific MS software.

Date:   Aug 19, 1982
        Revised Dec 7th, 1982
        Revised Jul 18, 1983

The  3.11  beta  test  versions  of  the  Microsoft languages Pascal and
FORTRAN ( and all subsequent versions  utilizing  the  i8087  )  require
special software  provided  by  the  OEM.  The OEM software is necessary
to initialize the 8087 coprocessor and its interrupt handler.


                            Flow of control
                            ---------------

The flow  of  control  between  Microsoft  software  and OEM software is
diagrammed below.


        |       Microsoft                       OEM
        |       ENTX??.ASM                      OEMR7.ASM
+---------------+                 +-------------+
|BEGXQQ:|       |                 |             |
|       |       |                 |             |
|       V       |                 |             |
|  +----------+ |                 |             |       OEMR7.ASM     INTR7.ASM
|  |  INIX87 ------------------------> OEMR87 --------> +---------+   +--------+
|  |    |     | |                 |      |      |       |         |   |        |
|  |    <--------------------------------+      |       | OEMI87 ---->| INTR87 |
|  |    |     | |                 |             |       |         |   |        |
|  |    |----------------------------> TSIR87   |       |         |   |   |    |
|  |    |     | |                 |      |      |       |   <---------|---+    |
|  |    <--------------------------------+      |       |         |   |        |
|  +----------+ |                 |             |       +---------+   +--------+
|       |       |                 |             |
|       |       |                 |             |
|     ENTGQQ    |                 |             |
|       |       |                 |             |
|       |       |                 |             |
|       V       |                 |             |
|  +----------+ |                 |             |
|  |  ENDX87  -----------------------> OEMS87   |
|  |    |     | |                 |      |      |
|  |    <--------------------------------+      |
|  |    |     | |                 |             |
|  |    |----------------------------> TSRR87   |
|  |    |     | |                 |      |      |
|  |    <--------------------------------+      |
|  +----------+ |                 |             |
|       |       |                 |             |
+---------------+                 +-------------+
        |
        V

                  Explaination of the flow of control.
                  ------------------------------------


Microsoft provides  an  entry  point module ENTX6?.ASM ( e.g. ENTX6L.ASM
).  All Microsoft programs begin execution at a label in ENTR??   called
BEGXQQ.   Control  passes  from  BEGXQQ  to  the  routine  INIX87 via an
indirect  long  call.    INIX87   is   the   Microsoft   provided   8087
initialization routine.   INIX87  provides  for  all machine independent
8087 initialization.  INIX87 calls OEMR87.

Because of the numerous ways in which  interrupts  may  be  mediated  in
an 8086-8087  system  (  e.g.  8259 interrupt controller, NMI connection
) only the Oem can  provide  the  proper  interrupt  interface.   OEMR87
is  an  OEM  PROVIDED  ROUTINE  which  performs  ALL  MACHINE  DEPENDENT
INTIALIZATION OF AN 8087.

It IS THE RESPONSIBILITY  OF  OEMR87  to  install  an  8087  exceptional
condition handler.  This handler, called OEMI87, calls an 8087 exception
routine , INTR7, provided by Microsoft.  It  IS  THE  RESPONSIBILITY  OF
OEMI87 to  ensure  that  the  8086  DS  register is equal to that set by
ENTX6?.ASM and to call INTR7 if the 8087 is the source of the  interrupt
( see  the  generic  example  below  ).   The routine INTR7 may be found
in the MS library module COMR7.ASM.

Flow of control returns to INIX87 from OEMR87.   INIX87  then  calls  an
OEM PROVIDED  ROUTINE  called  TSIR87  which  tests  the installation of
the 8087 interrupt handler.  TSIR87 may be a dummy routine  if  no  8087
interrupt installation test is desired.

Flow of control returns to INIX87 from TSIR87.   Flow  of  control  then
returns to  BEGXQQ  from  INIX87.   Control  then passes to ENTGQQ - the
main program.  When ENTGQQ terminates, control passes to ENDX87.  ENDX87
is  a  Microsoft  supplied  routine  which  reverses  any  special  8087
preparations done by INIX87.  ENDX87 calls OEMS87.   OEMS87  is  an  OEM
PROVIDED ROUTINE  which  reverses  ANY  AND  ALL  MACHINE DEPENDENT 8087
preparations done by OEMR87.  Flow of control  returns  to  ENDX87  from
OEMS87.   ENDX87  then  calls  an  OEM  PROVIDED  ROUTINE called TSRR87.
TSRR87 tests that the 8087 interrupt handler INTR87  has  been  removed.
TSRR87 may  be  a  dummy  routine  if  test is desired.  Flow of control
passes from TSRR87 to ENDR87.  Flow of control then passes  from  ENDR87
to the ENTX??  module and the program terminates.

There is a global double word EXCX87, which is used to count the  number
of times  the  Microsoft  supplied  interrupt  routine INTR7 is entered.
The variable EXCX87 is cleared by INIX87 before  TSIR87  is  called  and
is incremented by one each time INTR7 is entered.

TSIR87  is  a  function  that  returns  a  non-zero value in the 8086 AX
register if the installation  of  INTR7  was  successful.   Since  INTR7
increments EXCX87,  a possible test for successful installation of INTR7
would be to execute a software interrupt to  OEMI87  that  causes  INTR7
to be  called.   Upon  return  from the interrupt EXCX87 could be copied
to AX.

It is THE RESPONSIBILITY OF THE OEM to  set  the  global  byte  variable
CHPRQQ in  OEMX87.   If  non  ZERO,  this byte indicates the presence of
an 8087 in the system.  Both the 8087  runtime  and  the  8087  emulator
check the  status  of  this  byte.   To insure that the MS IEEE emulator
will always be used simply set CHPRQQ to ZERO in OEMR7.ASM.

Rather than  being  called  directly,  INIX87  and  ENDX87 are called by
ENTX6?  indirectly through  a  special  segment  EINQQQ.   This  segment
allows all 8087 functions to be "decoupled" from ENTX6?.

EINQQQ  SEGMENT WORD COMMON 'DATA'
InitializeCodeAddress   DD  INIX87
ExitCodeAddress         DD  ENDX87
EINQQQ  ENDS



                     A generic example of an OEMR87
                     ------------------------------
                              3.11 Release
                              ------------

The  following  is  a  generic  example  of  the module OEMR87.  In most
instances, only those portions of  the  following  module  dealing  with
interrupt dispatching  need be changed ( e.g. issuing an EOI instruction
to an 8259 controller ).  The example shows how  a  user's  DS  register
may be restored when 8087 interrupts occur.

;-----------------------------------------------------------------------
;
; OEMR87 - Oem dependent 8087 hardware initialization.
;
; This module contains any hardware dependent  code  necessary  for  the
; operation of  the  i8087  with MS languages.  This module installs the
; i8087 interrupt handler INTR87.  The procedures  in  this  module  are
; called from  INIX87  and  ENDX87 which are in turn called from ENTX??.
; The two word declaration of EXCX87 is required.
;-----------------------------------------------------------------------

NAME  OEMR87
TITLE OEMR87 -   OEM 8087 Interrupt     Handler      Installation
;                for MS-Pascal,Fortran.
PAGE

;-----------------------------------------------------------------------
;       MicroSoft supplied  8087  OEM  independent  interrupt   dispatch
;       routine.
;
EXTRN   INTR87:FAR

;-----------------------------------------------------------------------
;       MicroSoft end of program entry point.
EXTRN   ENDXQQ:FAR

;-----------------------------------------------------------------------
;       Utilities.
WASTETIME MACRO
        PUSH    AX
        POP     AX
        PUSH    AX
        POP     AX
ENDM

SAVEREG MACRO   R
IRP  PR,<R>
        PUSH    PR
ENDM
ENDM

RESTOREREG      MACRO   R
IRP  PR,<R>
        POP     PR
ENDM
ENDM

;---------------------------------------------------------------------
;       Assembly constants.
;---------------------------------------------------------------------

include     SYSI.ASM

PENDINGBIT      EQU     80H     ; 8087 interrupt pending bit.
TWOPOINTZERO    EQU     0       ;
CONTROLLER_PORT EQU     0       ; Guess at OEM controller port number.

IF PCDOS
   PORT_C       EQU     62H
ENDIF

IF PCDOS OR MSDOS OR SCP
i8087IntNum     EQU     02H
   OPSYS        EQU     21H
   SETVECOP     EQU     25H
   GETVECOP     EQU     35H
   CNTRLCOP     EQU     23H
   VERSIONOP    EQU     30H
ENDIF

IF OTHERS
   i8087IntNum  EQU     02H
ENDIF


;---------------------------------------------------------------------



DATA    SEGMENT PUBLIC  'DATA'

EXTRN   CHPRQQ:BYTE     ; this must be set to non 0 if 8087 is present and
                        ; it is to be used for fixup on the fly
PUBLIC  EXCX87
EXCX87  DW      0                       ; 8087 exception counter.
        DW      0

LABX87     DB      '<8087>'
EOIX87     DB      0
PRTX87     DB      0
SHRX87     DB      0
INTX87     DB      i8087intnum
INTOFFSET  DW      0

DATA    ENDS


OEMR87  SEGMENT  PUBLIC  'CODE'
DGROUP  GROUP   DATA
CGROUP  GROUP   OEMR87
        ASSUME CS:OEMR87,DS:DGROUP,SS:DGROUP,ES:DGROUP

;---------------------------------------------------------------------
;       Storage for initial Pascal-Fortran Data segment.
;       8087 control word.
ODVRQQ          DW      0       ; Old vector.
                DW      0

DATS87          DW      0
CTSR87          DW      0

EVEN
;---------------------------------------------------------------------
;       OEMI87 - OEM 8087 Interrupt procedure.
;
;       PROCEDURE OEMI87;
;
OEMI87  PROC    FAR

        PUSH AX                 ; Save DS of interrupt context.
        PUSH DS
        MOV  AX,CS:DATS87       ; Restore DS of user program.
        MOV  DS,AX
        
        ;
        ; Test for 8087 interrupt.
        ;
        FNSTSW CS:CTSR87
        WASTETIME
        TEST   CS:CTSR87,PENDINGBIT
        JZ     OVER8087         ; Not an 8087 interrupt.
                                ; Forward interrupt to old vector routine.

        SAVEREG         <BX,CX,ES,SI,DX,DI,BP>

        ;
        ; Must be an 8087 interrupt.
        ;
                                ; Make user   data   segment   available
                                ; to INTR87.
        MOV  ES,AX
        CALL INTR87             ; 8087 interrupt dispatch.

        MOV  AX,CS:DATS87
        MOV  DS,AX

        ;
        ; EOI -  End of interrupt command to interrupt dispatcher.
        ;
        AND     EOIX87,0FFH     ; Is the system configured as EOI.
        JZ      OVERI8259
        MOV     AL,EOIX87       ; Load up EOI instruction.
        XOR     DH,DH
        MOV     DL,PRTX87
        OUT     DX,AL           ; Reset 8259 interrupt controller.

        OVERI8259:

        RESTOREREG      <BP,DI,DX,SI,ES,CX,BX>

OVER8087:

        INC   EXCX87                     ; Count exceptions via this vector.
        JNO   O8087
        INC   EXCX87+2

O8087:

        TEST SHRX87,1
        JZ   DONE8087
        POP   DS
        POP   AX
        JMP   CS:(DWORD PTR ODVRQQ)      ; We should never return from here.

DONE8087:
        STI
        POP   DS
        POP   AX
        IRET

OEMI87 ENDP

;---------------------------------------------------------------------
;
;       OEMX87 - Perform OEM specific initialization of the 8087.
;
;       PROCEDURE OEMX87
;

PUBLIC  OEMX87
OEMX87  PROC   FAR

        ;
        ; Test for existence of 8087.
        ;
        MOV     BYTE PTR CHPRQQ,1       ; Chip is present if this is non-0
        FNINIT                          ; Initialize the 8087.
        XOR     AX,AX                   ; Clean AX.
        MOV     EXCX87,AX               ; Clear temporary.
        FNSTCW  EXCX87                  ; Issue 8087 instruction with no wait.
        WASTETIME                       ; Waste some time.
        OR      EXCX87,AX               ; Did any status word come back?

IFE     FRONTENDS                       ; Always use emulator for front ends.
        JNZ     GOT8087                 ; No 8087  present or 8087 malfunction.
ENDIF
        MOV     BYTE PTR CHPRQQ,0
        RET

GOT8087:
        SAVEREG       <BP,DX,ES,SI,DI,BX,AX,CX,DS>

        ; Initialize 8087 exception counter.
        ;
        XOR  AX,AX
        MOV  EXCX87,AX
        MOV  EXCX87+2,AX

        ; Save this executing programs DS.
        ;
        MOV CS:DATS87,SS

        MOV  AL,BYTE PTR INTX87         ;

        IF SCP OR PCDOS OR MSDOS OR OTHERS
        MOV  CS:(BYTE PTR INTINS+1),AL  ; Set up test interrupt number.
        ENDIF

        MOV  BYTE PTR INTOFFSET,AL      ; Set up interrupt offset.
        MOV  CL,2                       ;
        SAL  WORD PTR INTOFFSET,CL      ; *4

        ; Save old interrupt vector.
        ;
        IF PCDOS OR ( MSDOS AND TWOPOINTZERO )
        ;
        ; Ask operating system for vector.
        ;
        MOV     AL,BYTE PTR INTX87      ; Interrupt vector number.
        MOV     AH,GETVECOP             ; Operating system call interrupt.
        INT     OPSYS                   ; Call operating system.
        MOV     CS:ODVRQQ,BX            ; Squirrel aways old vector.
        MOV     CS:(ODVRQQ+2),ES

        ELSE

        ;
        ; Do a read into the vector space.
        ;
        PUSH    DS
        XOR     BX,BX                   ; Clear BX.
        MOV     AX,CS                   ; Set up DS:SI, ES:DI.
        MOV     ES,AX                   ; ES <-- CS.
        XOR     AH,AH                   ; Compute vector offset.
        MOV     SI,INTOFFSET            ;
        MOV     DS,BX                   ; DS <-- 0.
        CLI                             ; Disable 8086 interrupts.
        MOV     DI,OFFSET ODVRQQ        ;
        CLD                             ; Forward.
        MOVSW                           ; Move from   0:INTX87   to
        MOVSW                           ; CS:ODVRQQ.
        STI                             ; Restore 8086 interrupts.
        POP     DS
        ENDIF
        

        IF MSDOS OR PCDOS

        ; Have operating system intall interrupt vectors.
        ;
        MOV     DX,OFFSET OEMR87:OEMI87 ; Load DX with 8087 interrupt handler.
        MOV     AH,SETVECOP             ; Set interrupt vector code in AH.
        MOV     AL,BYTE PTR INTX87      ; Set vector number.
        MOV     CX,CS                   ; Move current CS to DS for opsys calls.
        MOV     DS,CX
        INT     OPSYS                   ; Install vector.
        MOV     DX,OFFSET OEMR87:CTCR87 ; Load DX with 8087 control C handler.
        MOV     AH,SETVECOP
        MOV     AL,CNTRLCOP
        INT     OPSYS                   ; Install vector.

        ELSE

        MOV     BP,SP                   ;
        MOV     DS,[BP]                 ; DS <-- Original DS.
        MOV     ES,BX                   ; ES <-- 0
        MOV     DI,INTOFFSET            ; Absolute vector address.
        MOV     AX,OFFSET OEMR87:OEMI87 ; Interrupt routine       offset
                                        ; ( by    convention    relative
                                        ; to the   current  cs:assume  ).
        CLI
        STOSW
        MOV     AX,CS                   ; Code segment.
        STOSW
        STI                             ; Restore 8086 interrupts.

        ENDIF
        

        RESTOREREG < DS,CX,AX,BX,DI,SI,ES,DX,BP>
        RET

PUBLIC  TSIR87

;--------------------------------------------------------------------
;       TSIR87 - Test installation of 8087 interrupt vector routine.
;       Suggestion:
;           If testing is undesirable, simply move 1 to AX.
;
;       PROCEDURE TSIR87;
;
TSIR87  LABEL FAR
        IF SCP OR PCDOS OR MSDOS OR OTHERS
INTINS: INT    i8087intnum
        ENDIF
        MOV    AX,DGROUP:EXCX87
        RET
OEMX87  ENDP

;---------------------------------------------------------------------
;       OEMS87 - OEM specific image rundown, 8087 clean up.
;       Called as part of ENDXQQ sequence.
;
;       PROCEDURE OEMS87;
;
PUBLIC  OEMS87
OEMS87  PROC  FAR
        ; Restore old interrupt vector.
        IF MSDOS OR PCDOS
        SAVEREG         <ES,DS,DX,AX>

        ; Was any vector saved to reinstall?
        ;
        LES  AX,CS:(DWORD PTR ODVRQQ)
        MOV  DX,ES
        OR   AX,DX
        JZ   NOTINSTALLED
        
        ; Request operating system to load vector.
        ;
        MOV  AH,SETVECOP
        MOV  AL,BYTE PTR INTX87
        LDS  DX,CS:(DWORD PTR ODVRQQ)
        INT  OPSYS
        RESTOREREG      <AX,DX,DS,ES>
        ELSE
        SAVEREG         <BX,CX,ES,DS,DI,SI>

        LES  BX,CS:(DWORD PTR ODVRQQ)
        MOV  CX,ES
        OR   CX,BX
        JZ   NOTINSTALLED
        
        CLI                             ; Disable 8086 interrupts.
        ; Load vector manually.
        ;
        XOR BX,BX                       ; Clear BX.
        MOV ES,BX                       ; Segment offset.
        MOV DI,INTOFFSET                ; Interrupt vector offset.
        PUSH CS                         ;
        POP  DS                         ;
        MOV SI,OFFSET ODVRQQ            ;
        CLD
        MOVSW                           ;
        MOVSW                           ;
        STI                             ; Enable 8086 interrupts.
        RESTOREREG      <SI,DI,DS,ES,CX,BX>
        ENDIF
        IF MSDOS OR PCDOS
        STC                             ; Set carry bit for ^C interrupt exit.
        ENDIF
NOTINSTALLED:
        RET

;--------------------------------------------------------------------
;       CTCR87 - Control C^ exit point.
PUBLIC  CTCR87
CTCR87  LABEL    FAR
        JMP      ENDXQQ  ; Jump back into ENTX6? and close files.


;

;--------------------------------------------------------------------
;       TSRR87 - Test removal of 8087 interrupt vector routine.
;       Suggestion:
;          If testing is undesirable, simply exit with a RET.
;
;       PROCEDURE TSRR87;
;
PUBLIC  TSRR87
TSRR87  LABEL FAR
        RET
OEMS87  ENDP

OEMR87  ENDS

END

SYSI.ASM
;-----------------------------------------------------------------------
; System switches definition file.
;
; Various versions  of  this file (e.g. with names sysiu.asm, sysil.asm,
; etc.)  exist.  The file  contains  definitions  of  assembly  switches
; used  by  other  runtime  routines  to  insert  special-case  code for
; particular systems.
;
; Runtime routines that need to know which system they are  being  built
; for should  include  the  file  "sysi.asm".  During the build process,
; the  proper  version  of  sysi.asm   should   be   copied   into   the
; currently-connected directory and given the name "sysi.asm".
;-----------------------------------------------------------------------

;-----------------------------------------------------------------------
; TRUE and FALSE.
;-----------------------------------------------------------------------
TRUE  EQU 1
FALSE EQU 0

;-----------------------------------------------------------------------
; Default radix for assembler.
;-----------------------------------------------------------------------
.RADIX  10

;-----------------------------------------------------------------------
; Define Operating system switches.
;-----------------------------------------------------------------------
XENIXKERNAL     EQU     FALSE    ; use in XENIX kernel only
XENIXRUNTIME    EQU     FALSE    ; use in XENIX runtime only (sysiu.asm)

PCDOS           EQU     FALSE    ; use in PCDOS environments (sysis.asm)

MSDOS           EQU     FALSE    ; use in MS-DOS environments (sysil.asm)
SCP             EQU     FALSE    ; Seattle Computer Products equipment

OTHERS          EQU     FALSE    ; CP/M 86 machines (sysim.asm)

;------------------------------------------------------------------------
; Define initial emulator interrupt number;  uses 10 consecutive vectors.
;------------------------------------------------------------------------

IF XENIXRUNTIME OR XENIXKERNAL
BEGINT  EQU     240; XENIXKERNAL beginning interrupt number.
ENDIF

IF MSDOS OR PCDOS
BEGINT  EQU     52
ENDIF

IF OTHERS
BEGINT  EQU     52
ENDIF

;-----------------------------------------------------------------------
; Encode-Decode Assembly Booleans.
;-----------------------------------------------------------------------

       FUDGE EQU FALSE;  Use 8087 BCD encode and constant instructions.
       LOG87 EQU TRUE ;  Use long multiplication log10 calculations.
  ROUNDTOINT EQU TRUE ;  Software or hardware supports 8087 round to integer.
    ESTIMATE EQU FALSE;  Estimated log - a calculus approximation.
   CHIPCONST EQU FALSE;  Use on chip 8087 constants.
    TESTING  EQU FALSE;
 SMALLTABLES EQU FALSE;  True if small but slow powers of ten function.
    EMULATOR EQU TRUE ;  True if emulator being used.
   DENORMALS EQU TRUE ;  True if denormals are supported.

;-----------------------------------------------------------------------
; Define debugging information flag.
;-----------------------------------------------------------------------
INSTRUMENTED EQU FALSE