.op
.pl72
.heUPDATE DISK NO. 3 / MS-DOS 2.11 (DM-V)     CS-SS      page #
              
    CONTENTS

    1.  DIRECTORY OF UPDATE DISK  .....................  2


    2.  CORRECTED UTILITIES

      2.1  BACKUP  ....................................  3

      2.2  RESTORE  ...................................  4


    3.  TOOLS

      3.1  ASCII  .....................................  5

      3.2  CHNGATTR....................................  5

      3.3  FORT87  ....................................  6

      3.4  PARKDMV  ...................................  6

      3.5  PRINTALL  ..................................  7

      3.6  RTC  .......................................  8

      3.7  SPEED  .....................................  8

      3.8  SPEEDNU  ...................................  9

      3.9  SWAPLPT  ...................................  9

      3.10 T8087  ..................................... 10
.PAŠ
    1.  DIRECTORY OF UPDATE DISK NO. 3



     Volume in drive A is DMV-2-11-U3   
     Directory of  A:\

    UPDATE   DOC     9472   8-22-86  12:00p

    BACKUP   COM     4278   2-08-85  12:00p
    RESTORE  COM     4188   2-08-85  12:00p

    ASCII    COM    10374   9-12-85  12:00p
    ASCII    PAS     3450   9-12-85  12:00p
    BACK     ASM      346   1-01-80  12:04a
    BACK     COM       20   3-10-86  12:36a
    CHNGATTR COM      720   9-12-85  12:00p
    FORT87   ASM      546   1-01-80  12:03a
    FORT87   COM       62   3-10-86  12:36a
    PARKDMV  COM      491  11-26-85  12:03a
    PRINTALL COM    20136   9-12-85  12:00p
    RTC      COM    11732   9-12-85  12:00p
    RTC      PAS     5412   9-12-85  12:00p
    SPEED    COM      765   9-12-85  12:00p
    SPEEDNU  COM      389   1-31-86   2:08p
    SWAPLPT  COM      139   9-12-85  12:00p
    T8087    COM       83   9-12-85  12:00p
       18 File(s)    277504 bytes free
.PAŠ
    2.  CORRECTED UTILITIES

    2.1  BACKUP

    PURPOSE

    Copies one fixed disk, a fixed disk unit or one or more files 
    from a fixed disk in the source drive to flexible disks.


    SYNTAX

    BACKUP [d1:] [<pathname>] [<filename> [.ext]]
            d2:  [/S/M/A/D:mm-dd-yy]


    COMMENTS

    see MS-DOS User's Guide p. 5-6

    CORRECTED PROBLEM

    The following configuration can lead to BACKUP failure:

    - One flex drive (A=B)  48 TPI
    - One hard disk drive C+D or C (10 MB)

    According  to  the  directory listing more than  360  KB  are 
    stored  on one BACKUP-diskette.  This diskette cannot be read 
    by  "RESTORE" ( Bad FAT - error ) and files on hard disk  can 
    be destroyed after restoring.

    The  described  problem  is  corrected  with   BACKUP/RESTORE 
    version with creation date 02-08-85.


    NOTE

    Same  version  of BACKUP as on Update Disk No.  1 for  MS-DOS 
    2.11.
.paŠ
    2.2  RESTORE


    PURPOSE

    Restores  backed-up files from a flexible disk to  the  fixed 
    disk.

    SYNTAX

    RESTORE d1: [d2:] [<pathname>] [<filename> [.ext]]
            [/S] [/P]


    COMMENTS

    see MS-DOS User's Guide p. 5-68

    CORRECTED PROBLEM

    The following configuration can lead to BACKUP failure:

    - One flex drive (A=B)  48 TPI
    - One hard disk drive C+D or C (10 MB)

    According  to  the  directory listing more than  360  KB  are 
    stored  on one BACKUP-diskette.  This diskette cannot be read 
    by  "RESTORE" ( Bad FAT - error ) and files on hard disk  can 
    be destroyed after restoring.

    The  described  problem  is  corrected  with   BACKUP/RESTORE 
    version with creation date 02-08-85.


    NOTE

    Same  version of RESTORE as on Update Disk No.  1 for  MS-DOS 
    2.11.
.PAŠ
    3.  TOOLS

    3.1  ASCII


    PURPOSE

    Transfers  WordStar files ( 8 bit code ) into ASCII-files ( 7 
    bit  code ) and removes all characters smaller than hex 20  ( 
    except 0D and 0A ).


    SYNTAX

    ASCII  ( menu driven )


    COMMENTS

    Program to delete any non-displayable ASCII characters from a 
    file.  The only characters allowed are hex 20 to hex 126, and 
    hex 0D and 0A.  The source file is not changed,  the filtered 
    information is written into a new file.  The program performs 
    I/O error checking to prevent file corruption.  No disk space 
    checking is performed.
    This  utility  can  also be used to make the  ASCII  part  of 
    ".COM"-files readable - for example screen messages.
    Non displayable characters are replaced by a period ("."),  a 
    set eight bit is forced to zero.
    Update disk contains Pascal source of program.
    

    NOTE

    This tool is not QA-tested and not supported !


    3.2  CHNGATTR    PURPOSE

    Displays and changes file-attributes.


    SYNTAX

    CHNGATTR (menue driven)


    COMMENTS

 "CHNGATTR" can  be used to look at the attribute of a  file  and 
    change the attribute.


    NOTE

    This tool is not QA-tested and not supported !

.paŠ
    3.3  FORT87


    PURPOSE

    The  RM/FORTRAN-compiler does not run on a DM-V.  It requests 
    the 8087-coprocessor,  but does not recognize it when using a 
    DM-V.  "FORT87" patches memory if a 8087 is present, to allow 
    RM/FORTRAN to make use of the 8087.


    SYNTAX

    FORT87          install patch
    ...  compiling  ...
    ...  running the program  ...
    BACK            uninstall patch


    COMMENTS

    The  patch  should always be uninstalled after compiling  the 
    FORTRAN-program and running the FORTRAN written  application, 
    in order to avoid conflicts with the operating system.


    NOTE

    This tool is not QA-tested and not supported !


    3.4  PARKDMV


    PURPOSE

    Diskrelocation


    SYNTAX

    PARKDMV


    COMMENTS

    This  diskrelocation  puts the DM-V into an halt state  after 
    locating the disk heads at a safe position.


    NOTE

    This tool is not QA-tested and not supported !

.paŠ
    3.5  PRINTALL


    PURPOSE

    Prints a group of files.


    SYNTAX

    PRINTALL  ( menu driven )


    COMMENTS

    This utility allows to print out files.
    The  user can switch drives,  path and filename  (  including 
    wildcard  characters ) within the utility.  Names of files to 
    be  printed  are displayed in alphabetical order  before  the 
    printout  starts,  allowing to discard single files from  the 
    queue, to change drive or path, or to quit.
    Files  containing control characters in the first sector  are 
    not printed.
    The  program  uses Form Feeds on the printer.  Tabs  are  not 
    expanded.


    NOTE

    This tool is not QA-tested and not supported !

.paŠ
    3.6  RTC


    PURPOSE

    Displays and sets Real Time - Clock.


    SYNTAX

    RTC   ( menu driven )


    COMMENTS

    Under  specific  circumstances it may be necessary to set  or 
    reset the Real Time - Clock.

    The  DM-V  MS-DOS  Real Time - Clock driver  uses  the  alarm 
    latches  for storing the year.  Programming an  alarm  causes 
    lost  of year in the system date and can result in system not 
    bootable.  After programming the Real Time - Clock you should 
    reset it for proper work with the system date.
    The utility is also contained as a Pascal listing to give  an 
    example of how to access the RTC.


    NOTE

    This tool is not QA-tested and not supported !


    3.7  SPEED


    PURPOSE

    SPEED  is  a  memory  resident  utility  which  substantially 
    improves the performance of many existing MS-DOS programs.


    SYNTAX

    SPEED ON        using SPEED
    SPEED OFF       disabling SPEED


    COMMENTS

    SPEED  is compatible with both MS-DOS 2.0 and 2.11.  The only 
    restriction  to  its  use  is that it  will  not  operate  in 
    conjunction with I/O redirection.


    NOTE

    This tool is not QA-tested and not supported !
.paŠ
    3.8  SPEEDNU


    PURPOSE

    Speed up Norton Utilities for DM-V


    SYNTAX

    SPEEDNU         install speed-up utility
    NU              start Norton Utilities


    COMMENTS

    SPEEDNU  loads a memory resident program for emulation of  an 
    industry compatible interrupt service routine ( INT 10H ).
    Switch "/D2" is not needed for running the Norton Utilities.


    NOTE

    This tool is not QA-tested and not supported !



    3.9  SWAPLPT


    PURPOSE

    Changes logical printer names in memory.


    SYNTAX

    SWAPLPT p1=p2


    COMMENTS

    p1, p2:   A digit in the range 1 to 5  ( LPT1 to LPT5 ).

    Delimiter  can be a "=" or any other character including  the 
    "space".


    EXAMPLE

    SWAPLPT 3=4   Changes LPT3 to LPT4 and vice versa.


    NOTE

    This tool is not QA-tested and not supported !
.paŠ
    3.10 T8087


    PURPOSE

    Check if 8087-coprocessor is included in system.


    SYNTAX

    T8087


    COMMENTS

    The utility uses 8087-code for checking, if there is an 8087-
    coprocessor installed.


    NOTE

    This tool is not QA-tested and not supported !