.MT2
.MB3
.OP
	     ZCPR - A Z80 Replacement for the CP/M CCP






     Documentation on ZCPR - A Z80 Replacement for the CP/M CCP




	      ZCPR is a	Group Project By the CCP-GROUP:
	    RLC	- Richard Conn		  FJW -	Frank Wancho
	    KBP	- Keith	Peterson	  RGF -	Ron Fowler


		      ZCPR Documentation By RLC










































Š			   Table of Contents
			  -----	-- --------

       Introduction					  2

       Part A: Installation Instructions		  4
	    ZCPR Integration Example			  5
	    Setting the	ZCPR Inline Options		  8
	      REL, BASE, CPRLOC, RAS, SUBA, CLEVEL3	  8
	    Customization Symbols			  8
	      NLINES, WIDE, PGDFLT			  8
	      PGDFLG, MAXUSR, SYSFLG, SOFLG, SUPRES,
		DEFUSR,	SPRMPT,	CPRMPT,	NUMBASE,	  9
		SECTFLG, FENCE				 10
	    Patching SUBMIT.COM				 10

       Part B: Usage Instructions and Explanation of
	       Commands					 11
	    The	ZCPR Command Hierarchy Search		 11
	    The	ZCPR-Resident Commands			 14
	      DIR, ERA					 14
	      LIST, TYPE, SAVE				 15
	      REN, USER, DFU				 16
	      JUMP, GO,	GET				 17
	    ZCPR Error Messages				 18

       Part C: ZCPR Command Levels and How to Use Them	 19








						Page 1
























Š	      ZCPR - A Z80 Replacement for the CP/M CCP



     Documentation on ZCPR - A Z80 Replacement for the CP/M CCP




       ZCPR is a replacement for the CP/M Console Command Processor 
  (CCP)	 which	is  designed to	run as part of	CP/M  on  Z80-based 
  microcomputers.   In most cases it is	upward-compatible with	the 
  original CP/M	Version	2.2 CCP.

       ZCPR,  however,	provides  many extensions to the CP/M  CCP.  
  Included in these extensions are the following features:

	    . The TYPE function	can be made to page or not page	its 
  output at the	user's discretion

	    .  A LIST function is available which sends	its  output 
  to the CP/M LST: Device and does NOT page

	    .  The  DIR	command	has been extended to allow the dis-
  play of the system files or all files

	    . The ERA command now prints out the names of the files 
  it is	erasing

	    .  The  current user number	may be included	as part	 of 
  the command prompt;  if the user is under a number other than	 0, 
  the prompt is	of the form 'du>' (like	'A2>' or 'B10>'),  and,	 if 
  the  user is under 0,	 the prompt may	be 'd>'	or 'd0>' as per	his 
  choice

	    .  The  SUBMIT facility has	been changed in	 two  basic 
  ways:
		 - the	prompt	changes	to 'du$' or 'd$'  when	the 
  SUBMIT command is printed
		 - the $$$.SUB is executed from	drive A: (note that 
  the  original	 SUBMIT	 problem now exists,  but the  new  SUB.COM 
  facility  corrects it);  the CCP-GROUP definition of an  Indirect 
  Command  File	 now  applies,	and this  definition  is  that	any 
  sequence of commands which may be issued from	the console is also 
  a  valid  sequence  of commands for execution	 from  an  Indirect 
  Command File;	hence, the sequence:

		      DIR
		      B:
		      DIR
		      A:

  may  be  issued  from	either the console or an  Indirect  Command 
  File,	 and the results of the	execution of this sequence are	the 
  same.	  Basically,  this  says  that Indirect	Command	 Files	are 
  upward-compatible  to	the console input (but not necessarily that 
  the  contents	 of an Indirect	Command	File may be issued  at	the 
  console without modification).


						Page 2Š




	     ZCPR - A Z80 Replacement for the CP/M CCP



	    .  A command-search	hierarchy is now implemented  which 
  is executed roughly as follows:
		 - the	user's command is checked against the  CPR-
  resident commands and	executed immediately if	a match	is found
		 - failing  that,  the	current	user number on	the 
  current disk is scanned for the COM file;  the COM file is loaded 
  and executed if found
		 - failing that, a default user	number (initially 0 
  but  can be reset with the DFU CPR-resident command) on the  cur-
  rent disk is scanned for the COM file; the COM file is loaded	and 
  executed if found
		 - finally,  failing that,  the	default	user number 
  on disk A:  is scanned for the COM file;  the	COM file is  loaded 
  and executed if found	or an error message (COMMAND?, when COMMAND 
  was the user's command name) is printed

	    .	The  numeric  argument for the SAVE command can	 be 
  specified  in	hexadecimal so that the	user may employ	the  values 
  presented by tools such as DDT exactly as they are given

	    .  A  GET  command which loads a file  at  a  specified 
  memory address and a JUMP command which "calls" the subroutine at 
  a  specified memory address have been	added;	a GO command  which 
  "calls"  the	subroutine at 100H (subset of the JUMP	capability) 
  has also been	added


       This  document provides the user	of ZCPR	with the  following 
  information:

	    Part A:  Installation Instructions
	    Part B:  Usage Instructions	and Explanation	of Commands
	    Part C:  ZCPR Command Levels and How to Use	Them


















						Page 3Š	      ZCPR - A Z80 Replacement for the CP/M CCP



			       Part A
		      Installation Instructions

       In  order to install ZCPR on a target microcomputer (must be 
  currently running CP/M 2.2), the user	must know two basic things:

	    1)	Where his CCP is currently running in memory
	    2)	Where his CCP is located in the	SYSGEN	image,	or, 
  for systems which don't support SYSGEN (such as P&T CP/M 2.2	for 
  the TRS-80 Model II),	where his CCP is located on disk and how to 
  place	the new	ZCPR on	top of it

       The  first question is answered relatively easily.   A  pro-
  gram,	 known	as either BDOSLOC or BDLOC (for	BDOS  Locator),	 is 
  provided  with ZCPR.	 You should assemble this program for  your 
  particular  computer (change the base	ORG if you are running non-
  ORG-0	CP/M) and execute it.	Upon execution,	it will	provide	you 
  with	the base address of (1)	the BDOS and (2) the CCP  for  your 
  particular system.   BDOSLOC has worked correctly for	all systems 
  tested so far,  but there is always a	chance that it may NOT work 
  for some non-tested system.	For the	time being,  assume that it 
  works	correctly and record the starting base page address of your 
  CCP.

       The  second question is not answered nearly so  easily.	 If 
  you  have  the ability to SYSGEN your	system,	 it is much  easier 
  (commonly) than if you do not.   You must,  after assembling	the 
  ZCPR	properly,  integrate it	into the sysgen	(or disk) image	 of 
  CP/M.	  This	can  be	 done by obtaining a SYSGEN image  of  your 
  system, scanning it via a debugger such as DDT to find the offset 
  for the CCP,	reading	the new	CPR in on top of the old  one,	and 
  finally  running  SYSGEN again to place the resultant	 system	 on 
  disk.	  If  you  DO NOT have SYSGEN capability,  a  Disk  Utility 
  program  is required to locate the CCP on disk and then write	the 
  new  ZCPR  on	 top  of the old  one.	 The  net  result  of  this 
  integration  is  the placement of the	new ZCPR onto disk  in	the 
  proper  place	so that	it will	be loaded with the rest	of CP/M	 on 
  cold boot and	executed properly.
       To find the original CCP, you typically have to locate it by 
  its appearance.   It is probably stored contiguously on disk,	so, 
  once it is found, a sequential overwrite is all that is required.  
  Probability  is extremely high that it is stored contiguously	 in 
  the SYSGEN image.   The CCP starts with two (2) and ONLY TWO jump 
  instructions	followed  by a buffer area (possibly containing	 an 
  initial  command and/or the Digital Research	copyright  notice).  
  The  Digital	Research manuals show the CCP to reside	at  address 
  980H	in the SYSGEN image,  but this may vary	 with  system.	 To 
  find	this image,  use DDT or	some other such	debugger,  load	the 
  SYSGEN image you can get via SYSGEN,	and examine memory starting 
  at around 900H for the two (and ONLY two) jumps described  above.  
  If  you find an area with more than two jumps	(a group of  them), 
  you  are probably looking at the BIOS	and should go lower for	the 
  CCP.	 The  CCP will probably	start on an even page or  half-page 
  address (like	900H, 980H, 1100H, etc).


						Page 4Š	      ZCPR - A Z80 Replacement for the CP/M CCP



       Now that	the location of	the CCP	has been found,	record this 
  address for later.  You are now ready	for the	integration of ZCPR 
  into your system.   To do this, perform the following	steps using 
  the  information  of the page	address	of the CCP  (obtained  from 
  BDOSLOC  and	called	CPRLOC within ZCPR) and	 the  SYSGEN  image 
  address of the CCP (called IMAGE for reference in this document).

	    1.	Edit  ZCPR  and	set the	CPRLOC equate to the  value 
  obtained from	above.	Also set any flags and values as you desire 
  (see the section on ZCPR Customization below).   When	 satisfied, 
  end the edit session.

	    2.	 Assemble  ZCPR	 with MAC  (or	equivalent).   This 
  assembler  is	 required  because of the MACROs  used.	  Only	the 
  resultant HEX	file is	required.

	    3.	 Assuming that you can use SYSGEN,  obtain a SYSGEN 
  image	of your	current	CP/M system and	save it	on disk.

	    4.	 Load  the  SYSGEN image into memory with  DDT	(or 
  equivalent).	Once loaded, verify that the original CCP is at	the 
  IMAGE	 address  found	above and compute  the	integration  offset 
  using	the DDT	H command:
		 H<IMAGE adr>,<CPRLOC adr>
  The  second number displayed gives you the OFFSET value  required 
  for step 5.

	    5.	 Integrate  ZCPR into your SYSGEN image	via DDT's I 
  and ROFFSET commands.	 Use IZCPR.HEX (or the name of your version 
  of  ZCPR) to load the	FCB and	ROFFSET	(where OFFSET was  computed 
  in  step 4) to load the ZCPR.HEX file	into memory at	the  proper 
  location.   Check  to	see that ZCPR is indeed	properly loaded	 by 
  examining the	SYSGEN IMAGE area.

	    6.	 Place the new system on disk by running SYSGEN	and 
  NOT loading the system from disk (use	the memory image).

       For   further  clarification  of	 the  above  process,	the 
  following  is	a sample terminal session which	outlines the  steps 
  taken.

		      ZCPR Integration Example


  B>; Sample terminal session for integrating ZCPR
  B>sysgen
  SYSGEN VER 2.2
  SOURCE DRIVE NAME (OR	RETURN TO SKIP)b
  SOURCE ON B, THEN TYPE RETURN	 <-- I hit the RETURN key here
  FUNCTION COMPLETE				   /
  DESTINATION DRIVE NAME (OR RETURN TO REBOOT)	<-- and	here
  B>save 44 cpm56.com	   <-- We now have a SYSGEN image of CP/M
				to work	with



						Page 5Š	      ZCPR - A Z80 Replacement for the CP/M CCP


  B>xdir
  XDIR	 Version 2.6  User Number:   0,	 Double	Density
  File Attributes:  Non-System	

  Filename.Typ Size K	Filename.Typ Size K   Filename.Typ Size	K
  -------- --- ------	-------- --- ------   -------- --- ------
  !TEXTWRK.-12	    0	CPR	.DOC	  8   EE687   .TXT	4
  CPR	  .AQM	   34	TFS	.HLP	  6   EE687PRE.TXT	4
  CPR	  .ASM	   50	CONTENTS.T01	  6   SW1     .TXT     10
  CPR	  .BAK	    4	CONTENTS.T02	  4   SW2     .TXT	2
  CPM56	  .COM	   12	CONTENTS.T03	  4
  B:  30 Entries &   22	Files --    338K Bytes Remaining
  File Data:	     14	Files --    154K Bytes Displayed
  B>bdosloc	 <-- Now to locate the CCP's address
  The Base Page	Address	of this	system's BDOS is C5
  The Base Page	Address	of this	system's CCP is	 BD <--	This is	it
  B>ddt	cpm56.com     <-- Now to find the CCP in the SYSGEN image
  DDT VERS 2.0
  NEXT	PC
  2D00 0100
  -d900,90f	 <-- Start looking around here
  0900 31 80 E7	3E 06 3C 3C FE 1B CA 00	C2 DA 11 E7 D6 1..>.<<.........
  -da00,a0f
  0A00 31 00 01	01 01 0C C5 CD 0F E4 21	00 BE 11 00 04 1.........!.....
  -db00,b0f
  0B00 31 00 01	01 01 11 C5 CD 0F E4 21	00 C0 11 00 02 1.........!.....
  -db80,b8f
  0B80 31 00 01	01 09 01 CD A8 00 21 00	D2 11 00 C2 0E 1........!......
	  -- Detail Left Out --
  -d1100	 <-- I found it	at 1100H; note the 2 JMP's
  1100 C3 FF BD	C3 FB BD 50 10 20 20 20	20 20 20 20 20 ......P.	       
  1110 20 20 20	20 20 20 20 20 00 00 00	00 00 00 00 00	       ........
  1120 00 00 00	00 00 00 00 00 00 00 00	00 00 00 00 00 ................
	  -- Detail Left Out --
  -^C		 <-- Return to CP/M; I know that CPRLOC	will be
		      BD00H and	the IMAGE offset is 1100H

  B>ed cpr.asm {edit ZCPR here and place CPRLOC=BD00H}#	 
	  -- Detail Left Out --

  B>mac	cpr $pz	sz	   <-- Now to assemble the CPR
  CP/M MACRO ASSEM 2.0
  C4F0			   <-- Note that CPR MUST end before BDOS
				begins!
  014H USE FACTOR
  END OF ASSEMBLY











						Page 6Š	      ZCPR - A Z80 Replacement for the CP/M CCP




  B>ddt	cpm56.com	   <-- Now to integrate!
  DDT VERS 2.0
  NEXT	PC
  2D00 0100
  -h1100,bd00		   <-- Compute offset for new CPR
  CE00 5400		   <-- Offset is 5400H
  -icpr.hex		   <-- Init FCB
  -r5400		   <-- Read in new CPR with offset
  NEXT	PC
  2D00 0000
  -^C			   <-- Done!
  B>sysgen		   <-- Now to SYSGEN onto disk
  SYSGEN VER 2.2
  SOURCE DRIVE NAME (OR	RETURN TO SKIP)	  <-- Use memory image
  DESTINATION DRIVE NAME (OR RETURN TO REBOOT)b	    <--	onto B:
  DESTINATION ON B, THEN TYPE RETURN
  FUNCTION COMPLETE
  DESTINATION DRIVE NAME (OR RETURN TO REBOOT) <-- Done	for now

  B>



































						Page 7Š	      ZCPR - A Z80 Replacement for the CP/M CCP



		   Setting the ZCPR Inline Options

       The  following  are the four basic options available to	the 
  user under ZCPR for customization of his package.

  Option Name	 Function

     REL	 Configures CPRLOC (CPRLOC equ 0) for integration
		 via MOVCPM rather than	the DDT/SYSGEN technique
		 outlined above; set to	TRUE for MOVCPM	integra-
		 tion or FALSE for DDT/SYSGEN integration

     BASE	 Base address of your CP/M system; standard CP/M
		 has a base of 0, but some CP/M	systems	(such as
		 for the TRS-80	Model I	and Heath/Zenith H89/Z89)
		 start physical	RAM memory at a	higher address;
		 equate	BASE to	the starting RAM memory	address	of
		 your system

     CPRLOC	 This is the starting address of ZCPR; set the
		 second	CPRLOC equate to the address you obtain
		 from BDOSLOC

     RAS	 This is an equate which masks out selected ZCPR
		 command functions for security	purposes on
		 Remote	Access Systems such as Bulletin	Boards;
		 the masked out	functions currently include
		 SAVE, ERA, REN, JUMP, GO, and GET; set	RAS to TRUE
		 to mask these out or FALSE to leave them in

     SUBA	 This is an equate which determines the	drive
		 onto which ZCPR will look for an executing
		 Indirect Command File.	 If the	basic philosophy
		 of the	Indirect Command File described	above is
		 to be maintained, this	symbol should be set to
		 TRUE (look on drive A:	for the	$$$.SUB	file); if
		 not, this symbol should be set	to FALSE (look on
		 the default drive from	the $$$.SUB file).  To
		 review, the basic philosophy of the Indirect
		 Command File is that any sequence of commands
		 which may be issued from the console (within
		 reason, which means NOT to erase a $$$.SUB file)
		 may also be issued from within	an Indirect
		 Command File, and the resultant execution should
		 be identical (same functions performed).

     CLEVEL3	 This equate enables or	disables extended Command
		 Level 3 Processing.  If set to	TRUE, extended
		 Command Level 3 Processing is enabled and the user
		 command line is automatically capitalized, the
		 terminating zero is placed at the end of the
		 buffer, and the internal CIBPTR is set	correctly
		 (see later for	more information).



						Page 8Š	      ZCPR - A Z80 Replacement for the CP/M CCP




			Customization Symbols

       The following symbols are provided for further customization 
  of ZCPR to a user's particular tastes	and hardware facilities.

  Option Name	 Function

     NLINES	 Number	of lines on the	user's CRT for paging

     WIDE	 This equate is	used to	select a narrow	or wide
		 display under the DIR command;	if WIDE	is equated
		 to TRUE, each file name is separated by two
		 spaces, a FENCE, and two more spaces; if WIDE is
		 equated to FALSE, each	file name is separated by
		 one space, a FENCE, and one more space

     PGDFLT	 This is the Paging Default flag for the TYPE
		 command; if PGDFLT is set to TRUE, the	TYPE
		 command will page its output by default and
		 the P option on the TYPE command (see below)
		 will prohibit paging; if PGDFLT is set	to FALSE,
		 the TYPE command will NOT page	its output by
		 default and the P option will enable paging

     PGDFLG	 This sets the option character	in the command
		 line for the TYPE command (the	'P' mentioned
		 above); if the	user wishes to change this option
		 character, he need only change	this equate

     MAXUSR	 This is the largest user number recognized by
		 the USER command; if the user wishes to protect
		 the higher user areas,	he may set this	symbol
		 to the	highest	area normally accessable; 15 is
		 the largest permitted value for MAXUSR

     SYSFLG	 This is the option character for the DIR command
		 line which is used to specify that DIR	search
		 All Files (both $SYS and $DIR)	for its	display;
		 the distributed default for this is 'A'

     SOFLG	 This is the option character for the DIR command
		 line which is used to specify that DIR	search
		 ONLY the $SYS files for its display; the distri-
		 buted default for this	is 'S'

     SUPRES	 Set SUPRES to TRUE to suppress	printing the user
		 number	when the user is under User Number 0 or
		 set SUPRES to FALSE to	ALWAYS display the User
		 Number	with the CPR prompt; with SUPRES set to
		 TRUE, a user on B: in user 0 sees 'B>'	as the
		 prompt, but with SUPRES set to	FALSE, a user on
		 B: in user 0 sees 'B0>' as the	prompt



						Page 9Š	      ZCPR - A Z80 Replacement for the CP/M CCP



     DEFUSR	 This is the CPR-default user number which is
		 searched in the command hierarchy for the COM
		 files (distributed as 0); the DFU changes this
		 temporarily until a Warm Boot or Cold Boot is
		 done, at which	time the search	reverts	to this
		 value

     SPRMPT	 This is the CPR prompt	character which	indicates
		 that a	SUBMIT file is in execution; by	default
		 it is set to '$', so prompts like 'A$'	appear
		 during	SUBMIT file execution

     CPRMPT	 This is the CPR prompt	character which	indicates
		 that the CPR is awaiting a user console command;
		 by default it is set to '>', so prompts like
		 'A>' appear during user input to the CPR

     NUMBASE	 This is the escape character used by those
		 commands which	require	a DECIMAL number as
		 an argument; placing this character after
		 the number argument switches the base to
		 HEXADECIMAL; for example, 'SAVE 15 MYFILE' can	be
		 expressed as 'SAVE FH MYFILE' if NUMBASE is
		 set to	'H' (the default)

     SECTFLG	 This character	constant is the	suffix option for
		 the SAVE command which	specifies that sectors,
		 as opposed to pages, are to be	saved; the default
		 value is 'S'

     FENCE	 This is the character printed to separate entries
		 in a directory	listing; it's default value is '|'


			 Patching SUBMIT.COM

       SUBMIT.COM  may be patched to run with ZCPR by the following 
  procedure  (this  is	recommended  if	 the  user  does  not  have 
  SUB.COM).   This  patch simply makes it always place the  $$$.SUB 
  file on Drive	A:.  Illustrative terminal session follows:

  A>ddt	b:submit.com
  DDT VERS 2.0
  NEXT	PC
  0600 0100
  -s5bb		  <-- Patch is at 5BB Hex
  05BB 00 1	  <-- Change 0 (default	drive) to 1 (drive A:)
  05BC 24 .	  <-- That's it!
  -d5b0	5cf	  <-- See change
  05B0 00 00 00	00 00 00 30 30 31 20 24	01 24 24 24 20 ......001 $.$$$ 
  05C0 20 20 20	20 53 55 42 00 00 00 1A	1A 1A 1A 1A 1A	   SUB.........
  -^C		  <-- Done
  A>save 5 newsubmt.com	  <-- Save new SUBMIT.COM file



						Page 10Š	      ZCPR - A Z80 Replacement for the CP/M CCP



			       Part B
	   Usage Instructions and Explanation of Commands


       The  following instructions are written with the	 assumption 
  that	the  reader is quite familiar with how to use CP/M 2.2	and 
  its CCP.   ZCPR is written as	a logical extension of the CP/M	2.2 
  CCP philosophy and should be addressed as such.



		  The ZCPR Command Hierarchy Search

       The first,  and most basic thing, to learn about	ZCPR is	the 
  order	in which is searches for a COM file for	execution or a file 
  specified  by	the GET	command.   Under the CP/M 2.2 CCP,  if	the 
  specified  COM file command was not found on the current drive in 
  the  current user area,  the CCP aborted with	an  error  message.  
  ZCPR,	 however,  continues searching from this point a maximum of 
  two  more  levels.   This command hierarchy search  was  outlined 
  above	and is described here in further detail.

	    1.	 If  the  command is of	the form 'COMMAND' and	NOT 
  'd:COMMAND',	the  CPR-resident  command list	is searched  for  a 
  match.   If  the  match is found,  the  CPR-resident	command	 is 
  immediately processed.   If the match	is not found or	the command 
  is  of the form 'd:COMMAND',	the next step is taken.	  Note that 
  the  'd:COMMAND'  form is good for executing a command  COM  file 
  which	 has the same name as a	CPR-resident command (such as  SAVE 
  or DIR).

	    2.	 If  the command is of the form	 'd:COMMAND',  disk 
  drive	 'd:'  is  temporarily logged in for  the  purpose  of	the 
  command  search.   Otherwise,	 the  currently	logged-in drive	 is 
  used.

	    3.	Now the	file named COMMAND.COM is searched for.	 If 
  found,  it  is loaded	into memory starting at	100H and  executed.  
  If not, proceed to step 4.

	    4.	 Now  that  the	first search  for  COMMAND.COM	has 
  failed,  the	CPR checks to see if the user is under the  current 
  Default User Number.	 The Default User Number may be	that set by 
  the  DEFUSR equate in	the CPR	or that	set by the user	via the	DFU 
  command.   DEFUSR  is	in effect if DFU has not been issued  since 
  the last Warm	or Cold	Boot, and DFU is in effect if it was issued 
  since	the last Warm or Cold Boot.   If the user is NOT under	the 
  current  Default User	Number,	 ZCPR temporarily logs him into	 it 
  and  searches	 the directory.	  If COMMAND.COM is  found,  it	 is 
  loaded as described above and	executed.  If not, ZCPR	proceeds to 
  the next step.





						Page 11Š	      ZCPR - A Z80 Replacement for the CP/M CCP



	    5.	 The user is now in the	Default	User Number, and at 
  this	point,	ZCPR checks to see if the user is on disk drive	A:.  
  If not, it temporarily logs into A: and searches the default user 
  number  of  A:  for  COMMAND.COM.   If found,	 it  is	 loaded	 as 
  described above and executed.	  If not,  ZCPR	prints the  command 
  name	as  an	error message and returns to  command  input  mode, 
  aborting the SUBMIT file if COMMAND came from	it.

       In  all cases of	the search above,  if COMMAND.COM is found, 
  after	 it  is	loaded into memory,  ZCPR resets the  user  to	his 
  original disk	drive and user number.	Hence, the files referenced 
  by the user by default are obtained from this	environment.

       To  illustrate this command hierarchy search,  consider	the 
  following examples:

  Example 1:  DEFUSR equ 0 {default user number	is 0}

  B10>		 <-- User is on	Drive B:, User Number 10
  B10>ASM TEST.BBZ    <-- User wishes to assemble TEST.ASM in
			   Drive B:, User 10
       <-- At this point, ZCPR looks on	B:/10 for ASM.COM, fails,
	    looks on B:/0, fails, and finally looks on A:/0; it
	    finds ASM.COM here and goes	back to	B:/10 for the file


  Example 2:  DEFUSR equ 0 and DFU issued

  B10>		 <-- User is on	Drive B:, User Number 10
  B10>DFU 5	 <-- User Selects User 5 as default
  B10>ASM TEST.BBZ    <-- As above
       <-- At this point, ZCPR looks on	B:/10 for ASM.COM, fails,
	    look on B:/5, fails, and finally looks on A:/5; it
	    fails here also and	prints ASM? as an error	message

  Example 3:  DEFUSR equ 0

  B>		 <-- User is on	Drive B:, User Number 0
  B>ASM	TEST.BBZ      <-- As above
       <-- At this point, ZCPR looks on	B:/0 for ASM.COM, fails,
	    looks on A:/0, fails, and prints error message

  Example 4:  DEFUSR equ 0

  A10>		 <-- User is on	Drive A:, User Number 10
  A10>ASM TEST.AAZ    <-- As above, but	file on	A:
       <-- At this point, ZCPR looks on	A:/10 for ASM.COM, fails,
	    looks on A:/0, fails, and prints error message








						Page 12Š	      ZCPR - A Z80 Replacement for the CP/M CCP



  Another Example:

	    For	 example,  if the user is logged into Drive  B:	 in 
  User Area 10,	the Default User Number	is 0, and the following	COM 
  files	are present as indicated --

		 WM.COM	on Drive A: in User 0
		 MBASIC.COM on Drive A:	in User	0 and on
		      Drive B: in User 0
		 TEST.COM on Drive B: in User 10 and Drive B:
		      in User 0

  then	the  following	happens	when  the  following  commands	are 
  issued from the console (or Indirect Command File):

  B10>WM TEST2.TXT
   \   \    \__	File to	be edited
    \	\__ Invoke the WM.COM file (Word Master	editor)
     \__ User is on Drive B: in	User Area 10

       Results:
	    ZCPR searches B:  User 10, B: User 0, and A: User 0	for 
  WM.COM;  it finds WM.COM in A:  User 0,  loads it,  logs the user 
  back into B: User 10,	and executes it.

  B10>MBASIC
   \	\__ Invoke the MBASIC.COM file (MBASIC Interpreter)
    \__	User is	on Drive B: in User Area 10

       Results:
	    ZCPR searches B:  User 10 and B: User 0 for	MBASIC.COM; 
  it finds MBASIC.COM in B: User 0, so it doesn't bother to look on 
  A:  User 0.	MBASIC.COM is then loaded and executed as described 
  in the previous example.

  B10>TEST
    \	\__ Invoke the TEST.COM	file (TEST program)
     \__ User is on Drive B: in	User Area 10

       Results:
	    ZCPR  searches  B:	User  10  for  TEST.COM;  it  finds 
  TEST.COM in B:  User 0,  so it doesn't bother	to look	further	(if 
  it had,  it would have found TEST.COM	in B: User 0).	TEST.COM is 
  then loaded and executed as described	above.

  B10>TEST2
    \	 \__ Invoke the	TEST2.COM file (TEST2 program)
     \__ User is on Drive B: in	User Area 10

       Results:
	    ZCPR searches B:  User 10, B: User 0, and A: User 0	for 
  TEST2.COM;  it  doesn't find it,  so it issues the error  message 
  'TEST2?', which says it couldn't find	TEST2.COM.



						Page 13Š	      ZCPR - A Z80 Replacement for the CP/M CCP





		     The ZCPR-Resident Commands

       The  following  pages describe the  ZCPR-Resident  Commands.  
  These	 are commands located within ZCPR itself which are executed 
  from within ZCPR.  The phrases <afn> and <ufn> refer to ambiguous 
  file name and	unambigous file	name as	per the	CP/M convention.

  Command: DIR
  Function:  To	Display	a listing of the names of the files on disk
  Forms:
       DIR <afn>	   <-- Displays	$DIR files
       DIR <afn> S	   <-- Displays	$SYS files
       DIR <afn> A	   <-- Displays	both $DIR and $SYS files
  Customization	Variables:
       WIDE	 SYSFLG	   SOFLG     FENCE
  Examples:
       DIR *.ASM	   <-- All $DIR	.ASM files
       DIR *.COM S	   <-- All $SYS	.COM files
       DIR *.COM A	   <-- All .COM	files
  Notes:
       If  a  file is scanned for and no such name exists on  disk, 
  the  'No  Files' message will	appear.	  However,  if	a  file	 is 
  scanned for and the name exists as a $SYS file and $DIR files	are 
  being	 scanned for,  no file name is displayed but the 'No Files' 
  message does NOT appear.  For	example, if TEST.COM is	a $SYS file 
  and  'DIR  TEST.COM' is issued,  no  message	appears.   If  'DIR 
  TEXT.COM' is issued and TEXT.COM does	not exist on disk,  the	'No 
  Files' message is displayed.


  Command: ERA
  Function:  To	Erase the specified $R/W files from disk
  Forms:
       ERA <afn>	   <-- Erase both $DIR and $SYS	files
  Customization	Variables:
       WIDE	 FENCE
  Examples:
       ERA *.ASM	   <-- Erase all .ASM files
       ERA *.*		   <-- Erase all files
  Notes:
       If a $R/O file is encountered,  a BDOS error message will be 
  displayed  and the procedure is stopped.   The user is unsure	 at 
  this	time as	to which files have been erased	and which have	not 
  and should check.  Sorry for this problem!  The ERASE	command	(to 
  be  given  to	SIG/M by RLC in	the near future) is a  solution	 to 
  this problem.








						Page 14Š	      ZCPR - A Z80 Replacement for the CP/M CCP




  Command: LIST
  Function:  To	Print the specified file on the	CP/M LST: device
  Forms:
       LIST <ufn>	   <-- Print the file (no paging)
  Customization	Variables:
       -None-
  Examples:
       LIST TEST.TXT	   <-- Print TEST.TXT on LST:
  Notes:
       If  the file has	a $SYS attribute,  it will be found as well 
  as those with	$DIR attributes.


  Command: TYPE
  Function:  To	Print the specified file on the	CP/M CON: device
  Forms:
       TYPE <ufn>	   <-- Print the file with the paging deflt
       TYPE <ufn> P	   <-- Print the file with the paging deflt
				negated
  Customization	Variables:
       NLINES	 PGDFLT	   PGDFLG
  Examples:
       TYPE TEST.TXT
       TYPE TEST.TXT P
  Notes:
       When  the  display pauses during	paging,	 type any  char	 to 
  continue or ^C to abort.  ^S also works.


  Command: SAVE
  Function:  To	Copy the TPA starting at 100H to disk
  Forms:
       SAVE <Number of Pages> <ufn>  <-- <Number of Pages> in DEC
       SAVE <Number of Pages>H <ufn> <-- <Number of Pages> in HEX
       SAVE <Number of Sectors>	<ufn> S	 <-- Number of sectors
       SAVE <Number of Sectors>H <ufn> S <-- Number of sectors
  Customization	Variables:
       NUMBASE	 RAS
  Examples:
       SAVE 15 MYFILE.TXT	 <-- 15	pages saved
       SAVE FH MYFILE.TXT	 <-- 15	pages saved
       SAVE 10H	MYFILE.TXT S	 <-- 16	sectors	(8 pages) saved
  Notes:
       If the file name	to be saved already exists,  then SAVE will 
  exit with the	message	'Delete	File?';	if the user REALLY wants to 
  save	under  this name,  he may then type Y or y and the  current 
  file will be deleted and then	recreated containing the  specified 
  part of the TPA.







						Page 15Š	      ZCPR - A Z80 Replacement for the CP/M CCP





  Command: REN
  Function:  To	Change the name	of a disk file
  Forms:
       REN <ufn	new>=<ufn old>
  Customization	Variables:
       RAS
  Examples:
       REN NEWFILE.TXT=OLDFILE.TXT
  Notes:
       If <ufn new> already exists, the	message	'Delete	File?' will 
  be  printed  and the user may	respond	with Y or y to	delete	the 
  current <ufn new> and	then rename <ufn old> to <ufn new>.

  Command: USER
  Function:  To	Change the current user	number
  Forms:
       USER <User Number>	<-- <User Number> in DEC
       USER <User Number>H	<-- <User Number> in HEX
  Customization	Variables:
       -None-
  Examples:
       USER 15	      USER FH	     USER 0
       USER	 <-- Same as USER 0
  Notes:
       -None-


  Command: DFU
  Function:  To	Temporarily Change the default user number for the
	     command hierarchy search
  Forms:
       DFU <User Number>	<-- <User Number> in DEC
       DFU <User Number>H	<-- <User Number> in HEX
  Customization	Variables:
       -None-
  Examples:
       DFU 15	      DFU FH	     DFU 0
       DFU	 <-- Same as DFU 0
  Notes:
       See above for explanation.














						Page 16Š	      ZCPR - A Z80 Replacement for the CP/M CCP





  Command: JUMP
  Function:  To	"call" the subroutine at the specified page address
  Forms:
       JUMP <Address> <Cmd Parms> <-- <Address>	in HEX
  Customization	Variables:
       NUMBASE	 RAS
  Examples:
       JUMP E000 or JUMP E000H	<-- Jump to E000H
       JUMP			<-- Jump to 000H
       JUMP 0			<-- Jump to 000H
  Notes:
       JUMP performs a subroutine "call", so the called	routine	may 
  return to the	ZCPR by	either a RET or	a Warm Boot.


  Command: GO
  Function:  To	"call" the subroutine starting at 100H
  Forms:
       GO <Cmd Parms>		<-- Execute reentrant at 100H
  Customization	Variables:
       RAS
  Examples:
       GO *.ASM			<-- Assuming XDIR is loaded,
				     gives directory of	*.ASM
  Notes:
       This  command is	identical in function to JUMP  100H;  JUMP, 
  however, leaves the address as the first entry in CP/M BASE +	80H 
  (the input line buffer), while GO has	no such	address.


  Command: GET
  Function:  To	load a file from disk into memory starting at the
	     specified page
  Forms:
       GET <Address> <ufn>	<-- <Address> in HEX
  Customization	Variables:
       NUMBASE	 RAS
  Examples:
       GET 8000	TEST.80		<-- Load TEST.80 starting at 8000H
       GET 100 TEST.80 or GET 100H TEST.80 <-- Load TEST.80	 
				     starting at 100H
       GET 0 TEST.80		<-- Load TEST.80 starting at 000H
  Notes:
       GET  searches for the specified file according to  the  same 
  command  hierarchy  search employed by the ZCPR command  scanner.  
  Hence,  if the user is on B:/10 and the file is on A:/0 with	the 
  current  default user	number at 0,  GET will search from B:/10 to 
  B:/0 to A:/0 in looking for the file.






						Page 17Š	      ZCPR - A Z80 Replacement for the CP/M CCP



			 ZCPR Error Messages

       The  following  are the error messages issued  by  ZCPR	and 
  their	meanings.

  Message   Meaning

  ?	    Printed after a command or an argument means that such
	      was invalid

  No File   From DIR, this means that DIR did not locate any files
	    Also from ERA with the same	meaning

  All?	    Issued in response ERA *.*,	asks the user is he really
	      wants to erase all the files.  Unlike under the
	      original CP/M 2.2	CCP, single character input is
	      required (Y or y for yes and anything else for no)
	      with NO <CR> to end the line

  Full	    From SAVE, means that there	is not enough space on
	      disk
	    From GET or	command	load by	CPR, means that	there
	      is not enough space in memory

  Delete File?
	    From REN or	SAVE, means that the file specified already 
	      exists on	disk and the user may type Y or	y to delete 
	      it and proceed with the REN or SAVE function




























						Page 18Š	      ZCPR - A Z80 Replacement for the CP/M CCP




			       Part C
	       ZCPR Command Levels and How to Use Them


       ZCPR  Version 1.0 and beyond supports three distinct command 
  levels in its	implementation.	 Each level constitutes	a different 
  way to issue a command for ZCPR to process.

       Command Levels 1	and 2 are common to all	implementations	 of 
  CP/M	and CP/ZM from CP/M Version 1.4.   Command Level 1 is  that 
  command level	in which the command is	issued by the user from	his 
  console  terminal.   The  prompt  'd>' or 'du>'  appears  on	the 
  terminal,  and  the  user  is	allowed	to enter the  command  with 
  editing from the terminal.  Command Level 2 is that command level 
  in which the command is entered from an executing $$$.SUB file.

       In  both	cases,	the command is stored in the internal  ZCPR 
  buffer called	CIBUFF (Command	Input BUFFer).	 Under both Command 
  Levels  1  and 2,  the command is placed into	 this  buffer,	the 
  characters of	the command line are capitalized, a character count 
  which	 indicates the number of characters in the command line	 is 
  stored in CBUFF (the byte before CIBUFF),  an	ending binary 0	 is 
  placed  after	 the last character in the command  line,  and	the 
  internal  pointer CIBPTR (Command Input Buffer PoinTeR) is set to 
  point	to CIBUFF (the first character of the command line).

       Command	Level 3	is an extended concept to Command Levels  1 
  and  2  which	is specifically	supported by ZCPR Version  1.0	and 
  beyond.  This	command	level allows a transient program to place a 
  command  line	into CIBUFF and	the character count into CBUFF	and 
  have this command line executed by ZCPR.   Once control is trans-
  ferred to ZCPR to execute the	command	line, the transient program 
  which	 placed	 the command line loses	control	and the	command	 is 
  executed  exactly as though it had been typed	by the user at	his 
  console terminal.

       In  order  for  a transient program to utilize  the  Command 
  Level	3 facility, this program MUST do the following:

	    1.	Locate the ZCPR.  Since	the ZCPR is ALWAYS 2K bytes 
  in  size and located directly	under the BDOS,	 the transient	can 
  locate  the  ZCPR  by	examining the BDOS entry  page	address	 at 
  location  7  and  subtracting	8 from this number (8  pages  =	 2K 
  bytes).  The resulting number	is the base page address of ZCPR.

	    2.	 Store the command line	in CIBUFF and the character 
  count	 in  CBUFF.   Knowing the base page address  of	 ZCPR,	the 
  following information	is useful in doing this:







						Page 19Š	      ZCPR - A Z80 Replacement for the CP/M CCP




		 ORG  CPRLOC	;Base Address of ZCPR
		 JMP  CPR	;Enter ZCPR and	Execute	Default	Cmd
		 JMP  CPR1	;Enter ZCPR and	Don't Execute
       MBUFF:	 DB   BUFLEN	;Size of CIBUFF	in bytes
       CBUFF:	 DS   1		;Number	of Bytes in Command Line
       CIBUFF:	 DS   BUFLEN	;Buffer	for Command Line
		 DS   1		;Buffer	for Ending 0 (set by ZCPR)
       CIBPTR:	 DS   2		;Address of CIBUFF (set	by ZCPR)


	    3.	 Obtain	 the User/Disk Flag.   Location	4  contains 
  this number,	but the	user may select	a flag of his choice.  This 
  flag	is  one	 byte  long,  and the high-order  nybble  (4  bits) 
  contains  the	user number and	the low-order nybble  contains	the 
  disk	number to process the command from.   The User/Disk Flag is 
  to be	passed to ZCPR in the C	Register.

	    4.	When ready, transfer control to	ZCPR to	process	the 
  command by JMPing to the base	address	of ZCPR.   The first JMP in 
  the JMP Table	given above is at this address.	 At this time, ZCPR 
  will	log in the user	and disk in the	User/Disk Flag and  process 
  the Command Level 3 Command Line.

































						Page 20Š	      ZCPR - A Z80 Replacement for the CP/M CCP




       The  following  is a sample program  which  illustrates	the 
  steps	outlined above:

  ;
  ;  Demonstration of Command Level 3 Facility by RLC
  ;
  udflag  equ	  4	  ;Address of User/Disk	Flag
  bdos	  equ	  5	  ;Address of BDOS Entry Point

	  org	  100h

	  lxi	  d,prmpt ;Print User Prompt
	  mvi	  c,9	  ;PRINT function
	  call	  bdos

	  lhld	  bdos+1  ;Get address of BDOS
	  mov	  a,h	  ;High-Order Address in A
	  sui	  8	  ;A=High-Order	Address	of CPR
	  mov	  h,a	  ;HL=Address of CPR
	  mvi	  l,0
	  shld	  cpr	  ;Save	address	in buffer

	  lxi	  d,6	  ;Point to command line buffer
	  dad	  d	  ;HL points to	command	line buffer
	  xchg		  ;DE points to	command	line buffer
	  mvi	  c,10	  ;READLN into this buffer
	  call	  bdos

	  lhld	  cpr	  ;Get Address of CPR
	  lda	  udflag  ;Get User/Disk Flag
	  mov	  c,a	  ; ...	in C
	  pchl		  ;Run Command Line

  cpr:	  ds	  2	  ;CPR Address buffer
  prmpt:  db	  'User	Command? $'






       Enjoy using ZCPR!
				-- RLC












						Page 21ŠUFLEN	;Buffer	for Command Line
		 DS   1		;Buffer	for Ending 0 (se