MODIFICATIOÎ TÏ FMT.COÍ TÏ ALLO× FORMAÔ OÆ EXTERNAÌ ADD-OÎ RIGIDS
                        WRITTEÎ 02/27/8µ 
Authorº			RUSÓ PENCIN
		 	SYSOÐ DALLAÓ CONNECTION
			(214© 783-768´ (ringback)

Thå followinç modificationó caî bå installeä usinç DDÔ anä musô be
installed in order to allow you to format the rigids that you have
added to the 820-II. 
The SA1403A controller will control up to 4 drives in any configuration.
It selects the drives as per the following table:

		Unit 0	=	00	(normaly the floppy)
		Unit 1	=	20	(add-on rigid #2)
		Unit 2	=	40	(add-on rigid #1)
		Unit 3	=	60	(system rigid)

To modify the FMT.COM program, bring it into memory using DDT:

		A>DDT FMT.COM
The sign-on should look like:
		0600 0100 xx
		-
Now modify the following locations using the S command:

		-S2F3 60 XX		(where XX is the new unit select)
		-S31A 60 XX		
		-S320 60 XX
		-S326 60 XX
		-^C
		A>save 5 FMTX.COM	(where X is the new unit character)

At this point you will need an FMTX.COM for each of your external rigids
because I haven't been able to add any user interface to select the drive
at run-time. Better this than nothing though.

If you should find that the values at these locations are not 60H, do a 
dump for 02F0 and locate the 60's that are offset by the same amounts as
the ones above. There is only one other 60H in the file and it is very
near the beginning and should not be changed.

The program RIGID1.COM sets the external rigid to be unit 1 (20H) and the
program RIGID2.COM sets one rigid to be unit 1 (20H), and the other to be
unit 2 (40H). 

Good luck with these mods, hope they make your new rigid extentions more
usable and easy to work with. If you have any problems, leave a message 
on my RCP/M describing the problem, and I will get back to you with fixes
or suggestions.

Russ Pencin
Dallas Connection RCP/M
(214) 783-7684 (ringback 24hrs. 300/1200 baud)
[eof]